## Slide 1: Atalanta: A Bit is Worth a “Thousand” Tensor Values
Alberto Delmas Lascorz, Mostafa Mahmoud, Ali Hadi Zadeh, Miloš Nikolić, Kareem Ibrahim, Christina Giannoula,
Ameer Abdelhadi, Andreas Moshovos
2024
Notes: - Hi I am Christina and I will briefly introduce our work
- Atalanta. [CLICK]

## Slide 2
Growing Memory Footprint of Deep Learning Models
E.g., Llama2: 7B Params, 26GB Mem
Cores
Off-Chip
Memory
GPU
bottleneck
Key Limitation:
Expensive Tensor Data Accesses from Off-Chip Memory
Data
1 0 0 1 0 1 0 1 1 1 0 0
0 1 1 0 0 0 1 0 1 0 0 1
1 1 0 0 1 0 0 1 1 0 0 0
1 0 0 1 1 0 1 0 1 0 0 1
Notes: - Nowadays,the memory footprint of state-of-the-art deep learning (DL) models has been rapidly increasing.
- As a result, the energy efficiency and execution performance of DL models is primarily limited by accesses to tensor data that resides in off-die memory modules. [CLICK]

## Slide 3
Atalanta: Overview
E.g., Llama2: 7B Params, 26GB Mem
Cores
Off-Chip
Memory
GPU
Atalanta:
A Near-Optimal Compression Engine for Deep Learning Models
Data
1 0 0 1 0 1 0 1 1 0 1 1 0 0
Notes: - To tackle this key limitation we propose Atalanta.
- a near-optimal, practical, hardware/software compression engine that significantly reduces the amount of data transferred between off-chip memory and processors. [CLICK]

## Slide 4
Atalanta: Brief Overview
Frequent values need less than 1 bit
  Arithmetic Coding [Langdon, 1984]
Cores
Off-Chip Memory
< 1 bit
Data
1 0 0 1 0 1 0 1 1 1 0 0
0 1 1 0 0 0 1 0 1 0 0 1
1 1 0 0 1 0 0 1 1 0 0 0
1 0 0 1 1 0 1 0 1 0 0 1
Notes: - Atalanta is inspired by Arithmetic Coding and our software compression strategy can encode frequent repeated data values using less than one bit. [CLICK]

## Slide 5
Atalanta: Brief Overview
Frequent values need less than 1 bit
  Arithmetic Coding [Langdon, 1984]
Low Hardware Costs
Cores
Off-Chip Memory
Compr. Unit
Compr. Unit
Compr. Unit
Data
1 0 0 1 0 1 0 1 1 1 0 0
0 1 1 0 0 0 1 0 1 0 0 1
1 1 0 0 1 0 0 1 1 0 0 0
1 0 0 1 1 0 1 0 1 0 0 1
< 50 bytes
Notes: - Our proposed compression units located just before the off-die memory controller,
have low power and area costs, each of them needs less than 50 bytes. [CLICK]

## Slide 6
Atalanta: Brief Overview
Frequent values need less than 1 bit
  Arithmetic Coding [Langdon, 1984]
Low Hardware Costs
Programmer Transparent
Lossless
Inference + Training (forward pass)
Cores
Off-Chip Memory
Compr. Unit
Compr. Unit
Compr. Unit
Vision
Image
Classification
Transformers
Notes: - Atalanta requres no modifications to Deep Learning Models
- is loseless in terms of accuracy
- and can be used for both inference and the forward pass of training. [CLICK]

## Slide 7
Atalanta: Brief Overview
Frequent values need less than 1 bit
  Arithmetic Coding [Langdon, 1984]
Low Hardware Costs
Programmer Transparent
Lossless
Inference + Training (forward pass)
High Compression Rate
Cores
Off-Chip Memory
Compr. Unit
Compr. Unit
Compr. Unit
Vision
Image
Classification
Transformers
Weights: 60% on average
Activations: 48% on average
Notes: - Across a wide range of Deep Learning models including GPT2 and Llama2 models
- Atalanta reduces data footprint of weights to 60%, and activations to 48% on average. [CLICK]

## Slide 8
Atalanta: Brief Overview
Frequent values need less than 1 bit
  Arithmetic Coding [Langdon, 1984]
Low Hardware Costs
Programmer Transparent
Lossless
Inference + Training (forward pass)
High Compression Rate
High Energy Efficiency
Cores
Off-Chip Memory
Compr. Unit
Compr. Unit
Compr. Unit
Vision
Image
Classification
Transformers
Notes: - Atalanta provides high energy efficiency. [CLICK]

## Slide 9
Atalanta: Brief Overview
Frequent values need less than 1 bit
  Arithmetic Coding [Langdon, 1984]
Low Hardware Costs
Programmer Transparent
Lossless
Inference + Training (forward pass)
High Compression Rate
High Energy Efficiency
Seamlessly Integrated with AI Accelerators
Tensor Cores
Off-Chip Memory
Compr. Unit
Compr. Unit
Compr. Unit
Vision
Image
Classification
Transformers
Performance: 1.44x
Energy Efficiency: 1.37x
Notes: - Finally, Atalanta can be easily integrated with DL accelerators at low cost.
- When integrated with a Tensorcore-based accelerator, Atalanta significantly improves performance and energy efficiency. [CLICK]

## Slide 10: Atalanta: A Bit is Worth a “Thousand” Tensor Values
Alberto Delmas Lascorz, Mostafa Mahmoud, Ali Hadi Zadeh, Miloš Nikolić, Kareem Ibrahim, Christina Giannoula,
Ameer Abdelhadi, Andreas Moshovos
2024
Notes: - Please attend our talk at ASPLOS 2024. Thank you.