## Slide 1
DCC Data-Centric Compilation of Machine Learning Kernels for Processing-In-Memory Architectures
Peiming Yang, Sankeerth Durvasula, Ivan Fernandez, Mohammad Sadrosadati, Onur Mutlu, Gennady Pekhimenko, Christina Giannoula ISCA 2026 Raleigh, USA, July 1st 2026

## Slide 2
Key Results: DCC improves performance by 1.7× and 1.3× over default implementation on HBM-PIM and AttAcc backends, respectively, for individual ML kernels, and by 2.0× over for LLM inference
Executive Summary
Problem: Host processors and PIM cores require different data layouts, thus necessitating expensive data rearrangements in ML kernel execution on PIM cores
DCC: The first data-centric ML compiler for PIM systems that jointly co-optimizes data rearrangements and compute code in a unified tuning process for multiple PIM backends
Key Components & Benefits:
Multi-Layer PIM Abstraction: enables support for multiple PIM backends
Data-Centric Schedule Generator: couples data and compute-loop partition strategies for co-optimization
PIM-Specific Code Optimizer: performs PIM-specific performance optimizations
Coupled Predictor: selects the best-performing configuration across joint data and compute-loop partition strategies
Intermediate Representation: provides a data-centric representation that can be lowered to multiple PIM backends
Prior Works: Current PIM compilation approaches lack systematic optimization of diverse ML kernels across multiple PIM backends and may largely ignore data rearrangement costs

## Slide 3
Background
DCC Design
Evaluation
Motivation
Talk Outline

## Slide 4
Large Language Models (LLMs):
Attention  always memory-bandwidth-bound
Fully-Connected (FC)  is memory-bandwidth-bound for certain batch sizes
Critical ML Kernels are Bottlenecked by Data Movement
Source: Y. He, et al., “PAPI: Exploiting Dynamic Parallelism in LLM Decoding with a PIM-enabled Computing System”, ASPLOS’24
OPT-30B Inference kernels on NVIDIA A100 GPU

## Slide 5
Processing-In-Memory (PIM) places processing units near memory arrays
Prior works (HBM-PIM [ISCA’21], AttAcc [ASPLOS’24], PAPI [ASPLOS’24]) design near-bank PIM systems for ML kernels
Near-bank PIM systems:
  Integrated with high-performance processor – Host xPU (e.g., GPU, TPU)
  Multiple PIM-enabled memory devices
  Low-power processing units (PIM core) close to one (or a few) memory bank(s)
  Immense aggregated memory bandwidth & High-levels of execution parallelism
PIM Alleviates Data Movement Bottlenecks
PIM Device
…
PIM Core
PIM Core
PIM Core
Mem. Bank(s)
Mem. Bank(s)
Mem. Bank(s)
PIM Device
Host xPU
(e.g., GPU, TPU)
Host Memory Space
Mem. Bank(s)
Mem. Bank(s)
Mem. Bank(s)
…
Memory Bank(s)
Processing Units
Registers
PIM Core
PIM Core
PIM Core
Mem. Bank(s)
Mem. Bank(s)
Mem. Bank(s)
…

## Slide 6
Host processors: consecutive elements are distributed across memory banks
PIM cores: consecutive elements are placed within local memory banks
  PIM cores can only access data from their local memory banks
Host xPU vs PIM Cores Require Different Data Layouts
PIM Device
…
PIM Core
PIM Core
PIM Core
Mem. Bank(s)
Mem. Bank(s)
Mem. Bank(s)
PIM Device
Host xPU
(e.g., GPU, TPU)
Host Memory Space
Mem. Bank(s)
Mem. Bank(s)
Mem. Bank(s)
…
PIM data layout
Host data layout
consecutive elements

## Slide 7
Input data rearrangements to place consecutive elements within the same banks for local PIM core processing
Computation execution on PIM cores
Output data rearrangements to merge partial results from step (2) or prepare output data for Host access
PIM Device
…
PIM Core
PIM Core
PIM Core
Mem. Bank(s)
Mem. Bank(s)
Mem. Bank(s)
PIM Device
Host xPU
(e.g., GPU, TPU)
Host Memory Space
Mem. Bank(s)
Mem. Bank(s)
Mem. Bank(s)
…
1
3
2
Three Steps of ML Kernel Execution on PIM Systems
Step
Step
Step

## Slide 8
DCC Design
Evaluation
Motivation
Background
Talk Outline

## Slide 9
Limitation 1: Existing compilers support a single PIM backend and/or optimize for a single ML kernel
PIM-DL [ASPLOS’24]  supports primarily UPMEM PIM backend & only GEMM kernel
ATiM [ISCA’24]  supports only UPMEM PIM backend
SimplePIM [PACT’23]  supports only UPMEM PIM backend
Cinm [ASPLOS’24]  supports primarily UPMEM PIM backend
PIMFlow [CGO’23]  supports only AiM PIM backend & only convolution kernel
Limitations of Existing PIM Compilers (I)

## Slide 10
Limitation 2: Existing compilers follow a compute-centric approach, and largely ignore data rearrangements costs during the compute-loop optimization step
 Treat data rearrangement costs as secondary, despite contributing significantly to total execution time
Limitations of Existing PIM Compilers (II)
def PIM_kernel:
for i in range(N1, N2):
for j in range(M1, M2):
for k in range(K1, K2):
A[i][j] = A[i+1][j*2] + B[j][k]
Core 1
for i in range(N):
for j in range(M):
for k in range(K):
A[i][j] = A[i+1][j*2] + B[j][k]
Compute-Centric Compiler
def PIM_kernel:
for i in range(N1, N2):
for j in range(M1, M2):
for k in range(K1, K2):
A[i][j] = A[i+1][j*2] + B[j][k]
Core 0
generates a fixed set of optimized compute-loop partition schemes for step
2
Phase 1
Phase 2
generates the corresponding data partition strategies for steps
1
3
selects the best-performing configuration within this fixed set of compute-loop and data partition strategies
Phase 3
def PIM_kernel:
for i in range(N1, N2):
for j in range(M1, M2):
for k in range(K1, K2):
A[i][j] = A[i+1][j*2] + B[j][k]
Core 1
def PIM_kernel:
for i in range(N’1, N’2):
for j in range(M’1, M’2):
for k in range(K’1, K’2):
A[i][j] = A[i+1][j*2] + B[j][k]
Core 0
Tensor A
Core 0
Core 1
…
Tensor A
Core 0
Core 1
…

## Slide 11
Performance comparison on a PIM system:
  Compute-centric TVM-based compiler (TVM) (following ATiM [ISCA’24]) vs
  Manually-tuned best-performing implementation (Best)
Limitations of Existing PIM Compilers (II)
Chart: Execution Time
| TVM | Best | TVM | Best | TVM | Best | TVM | Best | TVM | Best | TVM | Best | TVM | Best | TVM | Best | 16x2048 | 16x4096 | 28x2048 | 28x4096 | 16x256x2048 | 16x256x4096 | 28x256x2048 | 28x256x4096 | RED | GEMV
Compute Time | 0.10509 | 0.14122 | 0.070859 | 0.079717 | 0.083843 | 0.089956 | 0.089723 | 0.1509 | 0.54768 | 0.55701 | 0.60035 | 0.60521 | 0.56302 | 0.62059 | 0.59213 | 0.67992
Data Rearregement Time | 0.89491 | 0.57307 | 0.92914 | 0.53587 | 0.91616 | 0.52838 | 0.91028 | 0.80669 | 0.45232 | 0.30082 | 0.39965 | 0.24284 | 0.43698 | 0.27377 | 0.40787 | 0.23664
Slightly worse compute time could achieve much better data rearrangement time, thus resulting much better end-to-end kernel performance

## Slide 12
Co-Optimization of Compute-Loop and Data Partitioning is Needed
def PIM_kernel:
for i in range(N1, N2):
for j in range(M1, M2):
for k in range(K1, K2):
A[i][j] = A[i+1][j*2] + B[j][k]
Core 1
for i in range(N):
for j in range(M):
for k in range(K):
A[i][j] = A[i+1][j*2] + B[j][k]
Data-Centric Compiler  DCC
def PIM_kernel:
for i in range(N1, N2):
for j in range(M1, M2):
for k in range(K1, K2):
A[i][j] = A[i+1][j*2] + B[j][k]
Core 0
Single Phase
selects the best-performing configuration within jointly optimized compute-loop and data partition strategy combinations
def PIM_kernel:
for i in range(N1, N2):
for j in range(M1, M2):
for k in range(K1, K2):
A[i][j] = A[i+1][j*2] + B[j][k]
Core 1
def PIM_kernel:
for i in range(N’1, N’2):
for j in range(M’1, M’2):
for k in range(K’1, K’2):
A[i][j] = A[i+1][j*2] + B[j][k]
Core 0
Tensor A
Core 0
Core 1
…
Tensor A
Core 0
Core 1
…
Data rearrangement and compute code optimization are interdependent
def PIM_kernel:
for i in range(N1, N2):
for j in range(M1, M2):
for k in range(K1, K2):
A[i][j] = A[i+1][j*2] + B[j][k]
Core 1
def PIM_kernel:
for i in range(N’’1, N’’2):
for j in range(M’’1, M’’2):
for k in range(K’’1, K’’2):
A[i][j] = A[i+1][j*2] + B[j][k]
Core 0
Tensor A
Core 0
Core 1
…
generates and optimizes combinations of compute-loop and data partition strategies for all steps
2
1
3
less efficient compute strategy
best performance
cheaper data rearrangement strategy

## Slide 13
Evaluation
Background
Motivation
DCC Design
Talk Outline

## Slide 14
The first data-centric ML compiler for PIM systems that jointly co-optimizes compute-loop and data partition strategies into a unified tuning process
DCC Overview & 5 Key Components
DCC
ML Kernel with DCC API
HBM-PIM
SK Hynix AiM
AttAcc
Other PIM Backend …
1. Multi-Layer Abstraction
3. PIM-Specific Code Optimizer
2. Data-Centric Schedule Generator
4. Coupled Predictor
5. Intermediate Representation (IR)
DCC includes 5 key components and:
supports multiple PIM backends
supports any ML kernel
performs PIM-specific optimizations
is extensible for backend-specific and backend-agnostic optimizations
has low compilation time
consistently delivers near-optimal performance

## Slide 15
DCC Overview & 5 Key Components
QKV Generation
Attention
Projection
Feed-Forward
…
Layer 1
ML Model
DCC
ML Kernel with DCC API
HBM-PIM
SK Hynix AiM
AttAcc
Other PIM Backend …
1. Multi-Layer Abstraction
3. PIM-Specific Code Optimizer
2. Data-Centric Schedule Generator
4. Coupled Predictor
5. Intermediate Representation (IR)
 Provide a high-level (Python) interface to deploy ML kernels for PIM execution
Goal

## Slide 16
DCC Frontend Programming Interface - Python
1
2
3
4
5
6
7
@DCC_kernel
def PIM_kernel(A, B, C):
for i in range(0, 11, 1):
for j in range (0, 8, 1):
A[i][j] = A[i+1][j*2] + B[i] * C[j]
return A
ML Kernel with DCC API
Python

## Slide 17
@DCC_kernel
def example(A, B, C):
for i in range(0, 11, 1):
for j in range (0, 8, 1):
A[i][j] = A[i+1][j*2] + B[i] * C[j]
return A
class PIM_Layer(torch.nn.module, DCC.Layer):
def __init__(self, layer, input_sizes): # init kernel and weight
self.kernel = DCC.initKernel(PIM_kernel, input_sizes)
self.B = layer.B
self.C = layer.C
def update(self, best_draft): # pre-load data
self.PIM_B = self.kernel.preLoad(best_schedule, self.B)
self.PIM_C = self.kernel.preLoad(best_schedule, self.C)
def forward(self, x): # execute PIM kernel
return self.kernel(x, self.PIM_B, self.PIM_C)
model = torch.load("GPT3-13B.model") # load model
in_sizes=[[model.layer_0.B.sizes(), model.layer_0.C.sizes(),
model.input_sizes()]]
model.layer_0 = PIM_Layer(model.layer_0, in_sizes) # replace the layer
model = DCC.setModel(model) # collect model information
output = model(get_request()) # run the inference
DCC Frontend Programming Interface - Python
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
@DCC_kernel
def PIM_kernel(A, B, C):
for i in range(0, 11, 1):
for j in range (0, 8, 1):
A[i][j] = A[i+1][j*2] + B[i] * C[j]
return A
ML Kernel with DCC API
ML Model
Python
DCC necessary initializations

## Slide 18
DCC Overview & 5 Key Components
QKV Generation
Attention
Projection
Feed-Forward
…
Layer 1
ML Model
DCC
HBM-PIM
SK Hynix AiM
AttAcc
Other PIM Backend …
1. Multi-Layer Abstraction
3. PIM-Specific Code Optimizer
2. Data-Centric Schedule Generator
4. Coupled Predictor
5. Intermediate Representation (IR)
ML Kernel with DCC API
Enable support for multiple current and future PIM backends
Enable coarse-grained and fine-grained performance optimizations
Goal
1. Multi-Layer Abstraction

## Slide 19
We map PIM memory hierarchy into a compute hierarchy of 3 levels:
System level: Host xPU, Host memory spaces and multiple PIM devices
PIM group level: multiple PIM cores (and their local memory banks) belonging to the same memory channel or rank
PIM core level: the processing unit (core) and its local memory banks
1. Multi-Layer Abstraction for Near-Bank PIM Systems
Host xPU
(e.g., GPU)
Host Memory Space
Near-Bank PIM Devices
……
TG0
……
FPU
BK
BK
FPU
BK
BK
TG1
……
FPU
BK
BK
FPU
BK
BK
……
TG0
……
FPU
BK
BK
FPU
BK
BK
TG1
……
FPU
BK
BK
FPU
BK
BK
PIM Device 0
…
PIM Group 1
…
PIM Core 1
Mem. Bank(s)
PIM Core 1
Mem. Bank(s)
PIM Group 0
…
PIM Core 0
Mem. Bank(s)
PIM Core 1
Mem. Bank(s)
PIM Group 2
…
PIM Core 0
Mem. Bank(s)
PIM Core 1
Mem. Bank(s)
Memory Bank(s)
Processing Units
Registers

## Slide 20
HBM-PIM: Lee et al., “Hardware architecture and software stack for PIM based on commercial DRAM technology”, ISCA 2021 - Samsung
AttAcc PIM: Lee et al., “AttAcc! Unleashing the Power of PIM for Batched Transformer-based Generative Model Inference”, ASPLOS 2024
SK Hynix AiM: Lee et al., “Newton: A DRAM-Maker’s Accelerator-in-Memory (AiM) Architecture for Machine Learning”, MICRO 2020 – SK Hynix
Three Example PIM Backends into DCC’s Abstraction
Host xPU
(e.g., GPU)
Host Memory Space
PIM Memory Space
……
……
BK
BK
TG1
……
FPU
BK
BK
FPU
BK
BK
Near-Bank PIM Device
…
PIM Group 1
…
PIM Core 1
Mem. Bank(s)
PIM Core 1
Mem. Bank(s)
PIM Group 0
…
PIM Core 0
Mem. Bank(s)
PIM Core 1
Mem. Bank(s)
Abstraction
……
……
BK
BK
TG1
……
FPU
BK
BK
FPU
BK
BK
SK Hynix Aim
…
pCH 1
…
MAC Units
Mem. Bank
MAC Units
Mem. Bank
pCH 0
…
MAC Units
Mem. Bank
MAC Units
Mem. Bank
SK Hynix AiM
……
……
BK
BK
TG1
……
FPU
BK
BK
FPU
BK
BK
AttAcc PIM
…
pCH 1
…
GEMV Unit
Mem. Bank
GEMV Unit
Mem. Bank
pCH 0
…
GEMV Unit
Mem. Bank
GEMV Unit
Mem. Bank
AttAcc PIM
……
……
BK
BK
TG1
……
FPU
BK
BK
FPU
BK
BK
HBM-PIM
…
HBM-PIM
TG 0
…
FPU
Mem. Bank
Mem. Bank
FPU
Mem. Bank
Mem. Bank
TG 1
…
FPU
Mem. Bank
Mem. Bank
FPU
Mem. Bank
Mem. Bank

## Slide 21
DCC Overview & 5 Key Components
QKV Generation
Attention
Projection
Feed-Forward
…
Layer 1
ML Model
DCC
HBM-PIM
SK Hynix AiM
AttAcc
Other PIM Backend …
1. Multi-Layer Abstraction
3. PIM-Specific Code Optimizer
2. Data-Centric Schedule Generator
4. Coupled Predictor
5. Intermediate Representation (IR)
ML Kernel with DCC API
2. Data-Centric Schedule Generator
core-level
tiling drafts
 Generate candidate combinations of data partition strategies and compute-loop partition schemes for each PIM core
Goal
def PIM_kernel:
for i in range(N1, N2):
for j in range(M1, M2):
for k in range(K1, K2):
A[i][j] = A[i+1][j*2] + B[j][k]
Core 1
def PIM_kernel:
for i in range(N1, N2):
for j in range(M1, M2):
for k in range(K1, K2):
A[i][j] = A[i+1][j*2] + B[j][k]
Core 0
def PIM_kernel:
for i in range(N1, N2):
for j in range(M1, M2):
for k in range(K1, K2):
A[i][j] = A[i+1][j*2] + B[j][k]
Core 1
def PIM_kernel:
for i in range(N’1, N’2):
for j in range(M’1, M’2):
for k in range(K’1, K’2):
A[i][j] = A[i+1][j*2] + B[j][k]
Core 0
Tensor A
Core 0
Core 1
…
Tensor A
Core 0
Core 1
…
candidate tiling drafts
Draft 0. PIM Core 0: [(A[0:3][0:2], B[0:1][0:4] ...), (i ), (j ), (k )], ...
Draft 1. PIM Core 0: [(A[0:6][0:4], B[0:2][0:4] ...), (i ), (j ), (k )], ... Draft 4. PIM Core 0: [(A[0:6][0:2], B[0:1][0:4] ...), (i ), (j ), (k )], … …

## Slide 22
2. Data-Centric Schedule Generator
 Generate candidate data partition strategies, and derive corresponding compute-loop partition schemes for each PIM core
Goal
2A
Dimension Set Construction
2B
Data-Tile Construction
2C
Draft Pruning
2D
Data-Tile to Compute-Tile Mappings
Associates data partitions with compute-loop partitions
Generates all candidate data partitions across available PIM resources
Prunes unpromising data partition candidates to reduce tuning time
Constructs core-level data partitions and maps them to their corresponding compute-loop partitions on each PIM core
Draft 0. PIM Core 0: [(A[0:3][0:2], B[0:1][0:4] ...), (i ), (j ), (k )], ...
Draft 1. PIM Core 0: [(A[0:6][0:4], B[0:2][0:4] ...), (i ), (j ), (k )], ... Draft 4. PIM Core 0: [(A[0:6][0:2], B[0:1][0:4] ...), (i ), (j ), (k )], … …
candidate tiling drafts

## Slide 23
Challenge in Data-Centric Compilation Approach
How to associate data partitions to compute-loop partitions?
def PIM_kernel (A[6][8], B[4][4]):
for i in range(0, 5):
for j in range(0, 4):
for k in range(0, 4):
A[i][j] = A[i+1][j*2] + B[j][k]
Tensor A
Tensor B
data partitions
Core 0
Core 1
Core 0
Core 1
def PIM_kernel:
for i in range(?, ?):
for j in range(?, ?):
for k in range(?, ?):
A[i][j] = A[i+1][j*2] + B[j][k]
def PIM_kernel:
for i in range(?, ?):
for j in range(?, ?):
for k in range(?, ?):
A[i][j] = A[i+1][j*2] + B[j][k]
compute-loop partitions
Core 0
Core 1
?

## Slide 24
2A. Dimension Set Construction
associates data partitions with loop partitions
Dimension Set: a set of tensor dimensions indexed by the same loop, each through its own mapping function
def PIM_kernel (A[6][8], B[4][4]):
for i in range(0, 5):
for j in range(0, 4):
for k in range(0, 4):
A[i][j] = A[i+1][j*2] + B[j][k]
Tensor A
Tensor B
A1: 2rd dimension of A
A0: 1st dimension of A
B0
B1
A1  F(j) = j
A1  F(j) = j*2
B0  F(j) = j
B1  F(k) = k
A0  F(i) = i
A0  F(i) = i+1
3 dimension sets (one for each loop variable)
i loop variable
j loop variable
k loop variable
tensor dimension
corresponding mapping function
3 loop variables

## Slide 25
2B. Data-Tile Construction
generates all candidate data partitions across available PIM resources
DCC performs an exhaustive search to generate all data partitions for each dimension set
def PIM_kernel (A[6][8], B[4][4]):
for i in range(0, 5):
for j in range(0, 4):
for k in range(0, 4):
A[i][j] = A[i+1][j*2] + B[j][k]
A0  F(i) = i
A0  F(i) = i+1
3 dimension sets (one for each loop variable)
3 dimension sets (one for each loop variable)
A0  F(i) = i [repr.]
A0  F(i) = i+1
A0  F(i) = i
A0  F(i) = i+1 [repr.]
A1  F(j) = j
A1  F(j) = j*2
B0  F(j) = j
A1  F(j) = j [repr.]
A1  F(j) = j*2
B0  F(j) = j
A1  F(j) = j
A1  F(j) = j*2 [repr.]
B0  F(j) = j
A1  F(j) = j
A1  F(j) = j*2 B0  F(j) = j [repr.]
B1  F(k) = k [repr.]
B1  F(k) = k
3x
2x candidate representative mapping functions(A0i, A0i+1)
1x

## Slide 26
2B. Data-Tile Construction
generates all candidate data partitions across available PIM resources
DCC performs an exhaustive search to generate all data partitions for each dimension set
def PIM_kernel (A[6][8], B[4][4]):
for i in range(0, 5):
for j in range(0, 4):
for k in range(0, 4):
A[i][j] = A[i+1][j*2] + B[j][k]
A0  F(i) = i
A0  F(i) = i+1
available PIM resources: 2 PIM groups, 4 PIM cores per group
[1, 1]
[1, 3]
[1, 4]
[2, 1]
[1, 2]
[2, 2]
[2, 3]
[2, 4]
8x candidate PIM configurations [#PIM groups, #PIM cores per group]
#PIM groups
#PIM cores/ group
A0  F(i) = i [repr.]
A0  F(i) = i+1
A0  F(i) = i
A0  F(i) = i+1 [repr.]
exhaustive search
1st dimension set
[1, 1, A0i]
[1, 1]

## Slide 27
2B. Data-Tile Construction
generates all candidate data partitions across available PIM resources
DCC performs an exhaustive search to generate all data partitions for each dimension set
def PIM_kernel (A[6][8], B[4][4]):
for i in range(0, 5):
for j in range(0, 4):
for k in range(0, 4):
A[i][j] = A[i+1][j*2] + B[j][k]
Draft 0. [[1, 1, A0i], [1, 1, A1j], [1, 1, B1k]]
Draft 1. [[1, 1, A0i], [1, 2, A1j], [1, 1, B1k]]
Draft 2. [[1, 1, A0i], [1, 2, B0j], [1, 1, B1k]]
Draft 3. [[1, 1, A0i], [1, 2, A1j*2], [1, 2, B1k]]
Draft 4. [[1, 1, A0i], [1, 4, A1j*2], [1, 1, B1k]] Draft 5. [[1, 2, A0i], [1, 1, A1j], [1, 1, B1k]]
…
Draft 3070. [[2, 4, A0i+1], [2, 4, B0j], [2, 3, B1k]]
Draft 3071. [[2, 4, A0i+1], [2, 4, B0j], [2, 4, B1k]]
data-tile drafts
available PIM resources: 2 PIM groups, 4 PIM cores per group
(2x8) x (3x8) x (1x8) = 3072 drafts
2nd dimension set:
1 PIM group
1 PIM core per group
repr. mapping function: A1  F(j) = j
3rd dimension set:
1 PIM group
1 PIM core per group
repr. mapping function: B1  F(k) = k
[1, 1, A0i]
1st dimension set:
1 PIM group
1 PIM core per group
repr. mapping function: A0  F(i) = i

## Slide 28
2C. Draft Pruning
prunes unpromising data-tile drafts to reduce tuning time
DCC applies 3 pruning rules to significantly reduce the search space
def PIM_kernel (A[6][8], B[4][4]):
for i in range(0, 5):
for j in range(0, 4):
for k in range(0, 4):
A[i][j] = A[i+1][j*2] + B[j][k]
Draft 0. [[1, 1, A0i], [1, 1, A1j], [1, 1, B1k]]
Draft 1. [[1, 1, A0i], [1, 2, A1j], [1, 1, B1k]]
Draft 2. [[1, 1, A0i], [1, 2, B0j], [1, 1, B1k]]
Draft 3. [[1, 1, A0i], [1, 2, A1j*2], [1, 2, B1k]]
Draft 4. [[1, 1, A0i], [1, 4, A1j*2], [1, 1, B1k]] Draft 5. [[1, 2, A0i], [1, 1, A1j], [1, 1, B1k]]
…
Draft 3070. [[2, 4, A0i+1], [2, 4, B0j], [2, 3, B1k]]
Draft 3071. [[2, 4, A0i+1], [2, 4, B0j], [2, 4, B1k]]
data-tile drafts
typically 103 – 106 drafts
Draft 0. [[1, 1, A0i], [1, 1, A1j], [1, 1, B1k]]
Draft 1. [[1, 1, A0i], [1, 2, A1j], [1, 1, B1k]]
Draft 4. [[1, 1, A0i], [1, 4, A1j*2], [1, 1, B1k]] Draft 5. [[1, 2, A0i], [1, 1, A1j], [1, 1, B1k]]
…
Draft 3071. [[2, 4, A0i+1], [2, 4, B0j], [2, 4, B1k]]
pruning
pruned by ~95% (only ~5% retained)
pruned drafts
available PIM resources: 2 PIM groups, 4 PIM cores per group

## Slide 29
Draft 0. [[1, 1, A0i], [1, 1, A1j], [1, 1, B1k]]
Draft 1. [[1, 1, A0i], [1, 2, A1j], [1, 1, B1k]]
Draft 4. [[1, 1, A0i], [1, 4, A1j*2], [1, 1, B1k]] Draft 5. [[1, 2, A0i], [1, 1, A1j], [1, 1, B1k]]
…
Draft 3071. [[2, 4, A0i+1], [2, 4, B0j], [2, 4, B1k]]
constructs compute-loop partitions and data partitions for each PIM core for all drafts
def PIM_kernel (A[6][8], B[4][4]):
for i in range(0, 5):
for j in range(0, 4):
for k in range(0, 4):
A[i][j] = A[i+1][j*2] + B[j][k]
pruned drafts
Draft 0. [[1, 2, A0i], [2, 2, A1j*2], [1, 1, B1k]]
2D. Data-Tile to Compute-Tile Mappings
Draft 0. PIM Core 0: [(A[0:3][0:2], B[0:1][0:4] ...), (i ), (j ), (k )], PIM Core 1: [(A[0:3][2:4], B[1:2][0:4] ...), (i ), (j ), (k )], ...
core-level mappings
tensor dimensions
(len(A0)=6)
data-tile draft
(tile(A0i)=2)
def PIM_kernel (A[6][8], B[4][4]):
core-level compute-loop & data partitions
core-level tiling size
(len_per_core(A0)=3)

## Slide 30
Draft 0. [[1, 1, A0i], [1, 1, A1j], [1, 1, B1k]]
Draft 1. [[1, 1, A0i], [1, 2, A1j], [1, 1, B1k]]
Draft 4. [[1, 1, A0i], [1, 4, A1j*2], [1, 1, B1k]] Draft 5. [[1, 2, A0i], [1, 1, A1j], [1, 1, B1k]]
…
Draft 3071. [[2, 4, A0i+1], [2, 4, B0j], [2, 4, B1k]]
2D. Data-Tile to Compute-Tile Mappings
constructs compute-loop partitions and data partitions for each PIM core for all drafts
def PIM_kernel (A[6][8], B[4][4]):
for i in range(0, 5):
for j in range(0, 4):
for k in range(0, 4):
A[i][j] = A[i+1][j*2] + B[j][k]
pruned drafts
Draft 0. PIM Core 0: [(A[0:3][0:2], B[0:1][0:4] ...), (i ), (j ), (k )], PIM Core 1: ...
Draft 1. PIM Core 0: [(A[0:6][0:4], B[0:2][0:4] ...), (i ), (j ), (k )],
PIM Core 1: …
Draft 4. PIM Core 0: [(A[0:6][0:2], B[0:1][0:4] ...), (i ), (j ), (k )],
PIM Core 1: …
Draft 5. PIM Core 0: [(A[0:3][0:8], B[0:4][0:4] ...), (i ), (j ), (k )],
PIM Core 1: … ...
Draft 3071. PIM Core 0: [(A[0:1][0:1], B[0:1][0:1] ...), (i ), (j ), (k )],
PIM Core 1: …
core-level compute-loop partitions and data partitions for all dimension sets of all drafts
core-level tiling drafts

## Slide 31
DCC Overview & 5 Key Components
QKV Generation
Attention
Projection
Feed-Forward
…
Layer 1
ML Model
DCC
HBM-PIM
SK Hynix AiM
AttAcc
Other PIM Backend …
1. Multi-Layer Abstraction
3. PIM-Specific Code Optimizer
2. Data-Centric Schedule Generator
4. Coupled Predictor
5. Intermediate Representation (IR)
ML Kernel with DCC API
optimized core-level tiling drafts
3. PIM-Specific Code Optimizer
 Optimize performance of the pruned drafts  Be extensible to enable further backend-agnostic and backend-specific optimizations
Goal
optimized drafts
Draft 0. PIM Core 0: [(A[0:3][0:2], B[0:1][0:4] ...), (i ), (j ), (k )], ...
Draft 1. PIM Core 0: [(A[0:6][0:4], B[0:2][0:4] ...), (i ), (j ), (k )], ...
Draft 4. PIM Core 0: [(A[0:6][0:2], B[0:1][0:4] ...), (i ), (j ), (k )], … …
opt. strategy
opt. strategy
opt. strategy

## Slide 32
3. PIM-Specific Code Optimizer
optimizes performance of drafts & is extensible for further optimizations
Example: group-level broadcast commands in DCC
Host xPU
(e.g., GPU)
Host Memory Space
Near-Bank PIM Devices
……
TG0
……
FPU
BK
BK
FPU
BK
BK
TG1
……
FPU
BK
BK
FPU
BK
BK
……
TG0
……
FPU
BK
BK
FPU
BK
BK
TG1
……
FPU
BK
BK
FPU
BK
BK
PIM Group 0
PIM Core 1
Mem. Bank(s)
PIM Core 0
Mem. Bank(s)
PIM Core 3
Mem. Bank(s)
PIM Core 2
Mem. Bank(s)
PIM Group 1
PIM Core 1
Mem. Bank(s)
PIM Core 0
Mem. Bank(s)
PIM Core 3
Mem. Bank(s)
PIM Core 2
Mem. Bank(s)
data bus
command bus (READ, WRITE, MAC…)
MAC Core0_Group0 offset
MAC Core1_Group0 offset
MAC Core2_Group0 offset
MAC Core3_Group0 offset
naïve execution:
4 PIM cores /group ->
4 MAC commands
MAC_GROUP Group0 offset
optimized execution:
4 PIM cores / group ->
1 MAC group commands
4x commands
1x group-level broadcast command

## Slide 33
DCC Overview & 5 Key Components
QKV Generation
Attention
Projection
Feed-Forward
…
Layer 1
ML Model
DCC
HBM-PIM
SK Hynix AiM
AttAcc
Other PIM Backend …
1. Multi-Layer Abstraction
3. PIM-Specific Code Optimizer
2. Data-Centric Schedule Generator
4. Coupled Predictor
5. Intermediate Representation (IR)
ML Kernel with DCC API
predicted best-performing configuration
4. Coupled Predictor
 Estimate performance of all optimized drafts fast and accurately  Select the best-performing configuration
Goal
final best-performing configuration
Draft 4. PIM Core 0: [(A[0:6][0:2], B[0:1][0:4] ...), (i ), (j ), (k )], …
opt. strategy

## Slide 34
4. Coupled Predictor
accurately estimates performance of drafts & selects the best-performing configuration
DCC uses a learning-based performance predictor to enable fast & accurate predictions
optimized drafts
Draft 0. PIM Core 0: [(A[0:3][0:2], B[0:1][0:4] ...), (i ), (j ), (k )], ...
Draft 1. PIM Core 0: [(A[0:6][0:4], B[0:2][0:4] ...), (i ), (j ), (k )], ...
Draft 4. PIM Core 0: [(A[0:6][0:2], B[0:1][0:4] ...), (i ), (j ), (k )], … …
(trained) XGBoost Perf. Predictor
……
……
BK
BK
TG1
……
FPU
BK
BK
FPU
BK
BK
HBM-PIM
…
……
……
BK
BK
TG1
……
FPU
BK
BK
FPU
BK
BK
AttAcc PIM
…
pCH 1
…
GEMV Unit
Mem. Bank
GEMV Unit
Mem. Bank
pCH 0
…
GEMV Unit
Mem. Bank
GEMV Unit
Mem. Bank
……
……
BK
BK
TG1
……
FPU
BK
BK
FPU
BK
BK
SK Hynix Aim
…
pCH 1
…
MAC Units
Mem. Bank
MAC Units
Mem. Bank
pCH 0
…
MAC Units
Mem. Bank
MAC Units
Mem. Bank
SK Hynix AiM
AttAcc PIM
HBM-PIM
TG 0
…
FPU
Mem. Bank
Mem. Bank
FPU
Mem. Bank
Mem. Bank
TG 1
…
FPU
Mem. Bank
Mem. Bank
FPU
Mem. Bank
Mem. Bank
opt. strategy
opt. strategy
opt. strategy
PIM backend information
pred. time: 10ms
pred. time: 60ms
pred. time: 20ms
predicted time
final best-performing configuration
Draft 0. PIM Core 0: [(A[0:3][0:2], B[0:1][0:4] ...), (i ), (j ), (k )], …
opt. strategy

## Slide 35
DCC Overview & 5 Key Components
QKV Generation
Attention
Projection
Feed-Forward
…
Layer 1
ML Model
DCC
HBM-PIM
SK Hynix AiM
AttAcc
Other PIM Backend …
1. Multi-Layer Abstraction
3. PIM-Specific Code Optimizer
2. Data-Centric Schedule Generator
4. Coupled Predictor
5. Intermediate Representation (IR)
ML Kernel with DCC API
 Capture optimized data partition strategies and compute-loop partition schemes  Enable support for multiple current & future PIM backends
Goal
%a_core[%i,%j] =
%a_core[%i+1,%j*2] + %b_core[%j][%k] …
DCC IR
%reg_a=load %a_core[%i+1,%j*2]
%reg_sum=ADD %b_core[%j][%k],%reg_a …
backend PIM instructions
5. Intermediate Representation (IR)

## Slide 36
5. Intermediate Representation (IR)
captures data and compute-loop partition strategies & enables multi-PIM-backend support
@DCC_kernel
def example(A, B, C):
for i in range(0, 5):
for j in range(0, 4):
for k in range(0, 4):
A[i][j] = A[i+1][j*2] + B[j][k]
return A
2. Data-Centric Schedule Generator
4. Coupled Predictor
3. PIM-Specific Code Optimizer
best-performing config.
@hardware_platform[GROUPS=2, CORES=4]
func @example(%a:<6x8xfp32>, %b:<4x4xfp32>): <6x8xfp32>
complex_dimset %ds_i {
%dim[0] = %a.dim[0] -> i,
%dim[1] = %a.dim[0] -> i+1 [representative] }
%ds_i.range = (0, 5, 1)
complex_dimset %ds_j {
%dim[0] = %a.dim[1] -> j,
%dim[1] = %a.dim[1] -> j*2 [representative],
%dim[2] = %c.dim[0] -> j }
%ds_j.range = (0, 4, 1)
complex_dimset %ds_k {
%dim[0] = %b.dim[1] -> k }
%ds_k.range = (0, 4, 1)
data_tile %dt_i: (1,2) -> (1,2,3)
data_tile %dt_j: (2,2) -> (2,2,1)
data_tile %dt_k: (1,1) -> (1,1,4)
compute_tile %ct_i: (1,2,6) -> [[{0,1,2}, {3,4,5}]]
compute_tile %ct_j: (2,1,4) -> [[{0}], [{1}], [{2}], [{3}]]
compute_tile %ct_k: (1,1,4) -> [[{0,1,2,3}]]
tensor_indices %tt_i: %ct_i -> [[{0,1,2,3}, {3,4,5,6}]]
tensor_indices %tt_j: %ct_j -> [[{0}], [{1,2}], [{2,4}], [{3,6}]]
tensor_indices %tt_k: %ct_k -> [[{0,1,2,3}]]
%a_core = rearrange %a -> %tt_i, %tt_j [to_PIM_core]
%b_core = rearrange %b -> %tt_i, %tt_k [to_PIM_core]
parallel_PIM (GROUPS, CORES) {
loop (i, j) in (%ct_i, %ct_j, %ct_k) {
%a_core[%i, %j] = %a_core[%i+1, %j*2] + %b_core[%j][%k]
}}
%a_out = rearrange %a_core -> %a [to_host]
ret %a_out
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
DCC IR
%a_core[%i, %j] = %a_core[%i+1, %j*2] + %b_core[%j][%k]
backend PIM instructions
%reg_a = load %a_core[%i+1, %j*2]
%reg_b = load %b_core[%j][%k]
%reg_sum = ADD %reg_b, %reg_a
store %reg_sum -> %a_core[%i, %j]
%reg_a = load %a_core[%i+1, %j*2]
%reg_sum = ADD %b_core[%j][%k], %reg_a
store %reg_sum -> %a_core[%i, %j]
AttAcc PIM Instructions
HBM-PIM Instructions

## Slide 37
DCC Design
Background
Motivation
Evaluation
Talk Outline

## Slide 38
Evaluation Methodology
Simulation Methodology:
  Modified simulator using AttAcc [ASPLOS’24] and Ramulator 2.0 [IEEE CAL’23]
  NVIDIA A100 GPU with 5 PIM-enabled HBM3 devices (80GB memory in total)
2× PIM Backends:
  AttAcc [ASPLOS’24]
  HBM-PIM [ISCA’21]
5× ML Kernels (kernel evaluation):
  AttAcc: GEMV, RED, ATTN
  HBM-PIM: GEMV, RED, VA, RELU
3× ML Models (end-to-end inference evaluation): GPT3-13B, LLAMA2-33B, MT-NLG-310B
Comparison Points:
  GPU: GPU-only execution (NVIDIA A100)
  AttAcc: Original open-source AttAcc PIM implementation
  AttAcc+DCC: AttAcc PIM backend with DCC compilation
  HBM-PIM: HBM-PIM backend using AttAcc’s data partition strategy
  HBM-PIM+DCC: HBM-PIM backend with DCC compilation

## Slide 39
ML Kernel Performance on AttAcc PIM Backend
Chart: Speedup over GPU
| ATTN | GEMV | RED | ATTN | GEMV | RED
AttAcc | 8.9011 | 7.5076 | 6.248 | 5.3312 | 1.0178 | 1.0178
AttAcc+DCC | 10.8722 | 9.868 | 7.7862 | 7.4406 | 1.6899 | 1.4917
batch size = 1
batch size = 4
DCC on AttAcc improves performance of individual ML kernels by up to 1.7× and 1.3× on average over AttAcc with its fixed data partitioning method

## Slide 40
ML Kernel Performance on HBM-PIM PIM Backend
Chart: Speedup over GPU
| GEMV | RELU | RED | VA | GEMV | RELU | RED | VA
HBM-PIM | 3.8209 | 1.3676 | 0.5199 | 0.98563 | 3.1118 | 1.6716 | 0.63539 | 1.2047
HBM-PIM+DCC | 5.66 | 2.433 | 1.2186 | 1.9505 | 5.5244 | 2.7076 | 1.3869 | 2.0797
batch size = 1
batch size = 4
DCC on HBM-PIM improves performance of individual ML kernels by up to 2.1× and 1.7× on average over HBM-PIM with its fixed data partitioning method

## Slide 41
Chart: Normalized Execution Time
| GPU | AttAccBase | AttAccBase+DCC | AttAccFull | AttAccFull+DCC | GPU | AttAccBase | AttAccBase+DCC | AttAccFull | AttAccFull+DCC | GPU | AttAccBase | AttAccBase+DCC | AttAccFull | AttAccFull+DCC | GPU | AttAccBase | AttAccBase+DCC | AttAccFull | AttAccFull+DCC | GPT3-13B | LLAMA2-33B | GPT3-13B | LLAMA2-33B | batch size = 1 | batch size = 4
Attention | 0.14197 | 0.0068777 | 0.0063944 | 0.0068777 | 0.0063944 | 0.091256 | 0.0077091 | 0.0064311 | 0.0077091 | 0.0064311 | 0.24527 | 0.022139 | 0.019281 | 0.022139 | 0.019281 | 0.15814 | 0.021554 | 0.019466 | 0.021554
QKV Generation | 0.19599 | 0.19599 | 0.029424 | 0.19096 | 0.024748 | 0.21674 | 0.21674 | 0.041523 | 0.21107 | 0.036793 | 0.17206 | 0.17206 | 0.098593 | 0.15587 | 0.084494 | 0.18975 | 0.18975 | 0.12905 | 0.1739 | 0.11474
Projection | 0.065337 | 0.065337 | 0.0088574 | 0.063661 | 0.0072988 | 0.072255 | 0.072255 | 0.012305 | 0.070365 | 0.010728 | 0.057384 | 0.057384 | 0.030013 | 0.051988 | 0.025313 | 0.063276 | 0.063276 | 0.038024 | 0.057991 | 0.033251
Feed-forward | 0.52181 | 0.52181 | 0.52181 | 0.030694 | 0.030694 | 0.57191 | 0.57191 | 0.57191 | 0.033642 | 0.033642 | 0.45809 | 0.45809 | 0.45809 | 0.091618 | 0.091618 | 0.54592 | 0.54592 | 0.54592 | 0.10918 | 0.10918
Other | 0.073801 | 0.073801 | 0.073801 | 0.073801 | 0.073801 | 0.04713 | 0.04713 | 0.04713 | 0.04713 | 0.04713 | 0.065292 | 0.065292 | 0.065292 | 0.065292 | 0.065292 | 0.041691 | 0.041691 | 0.041691 | 0.041691 | 0.041691
LLM Inference Performance on AttAcc PIM Backend
AttAccBase: AttAcc PIM fully running attention on PIM cores
AttAccFull: AttAcc PIM running both attention and a part of feed-forward on PIM cores
7.00
7.42
3.50
3.14
DCC accelerates LLM inference by up to 2.7× and 2.0× on average over AttAcc with its default fixed partitioning method

## Slide 42
More Evaluations in the Paper
Detailed ML kernel analysis with various tensor sizes and batch sizes
Scalability analysis on large batch sizes
Detailed LLM inference results with various input token, output token, and batch sizes
Large-scale LLM inference performance with FP8 and FP16 precisions
Energy consumption evaluation on LLM inference with various input token, output token, and batch sizes
Compilation time analysis on various ML kernels, LLMs and PIM hardware resources
Effectiveness of the DCC’s pruning mechanisms
Accuracy, compilation analysis and performance analysis of the DCC predictor
Performance analysis of DCC in LLM inference with dynamic tensor sizes

## Slide 43
DCC is Open Source & Awarded with all 3 Eval. Badges
DCC
Paper
GitHub
https://github.com/SPIN-Research-Group/DCC

## Slide 44
Conclusion
DCC: The first data-centric ML compiler for PIM systems that jointly co-optimizes data rearrangements and compute code in a unified tuning process and supports any ML tensor kernel and multiple PIM backends
Key Contributions:
Enables support for multiple PIM backends
Couples data and compute-loop partition strategies for co-optimization
Performs PIM-specific performance optimizations
Provides the best-performing configuration across joint data and compute-loop partition strategies
Integrates a data-centric intermediate representation that can be lowered to multiple PIM backends
DCC
Key Results: DCC improves performance by 1.7× and 1.3× over default implementation on HBM-PIM and AttAcc backends, respectively, for individual ML kernels, and by 2.0× over AttAcc default implementation for LLM inference
Paper
GitHub

## Slide 45
DCC Data-Centric Compilation of Machine Learning Kernels for Processing-In-Memory Architectures
Peiming Yang, Sankeerth Durvasula, Ivan Fernandez, Mohammad Sadrosadati, Onur Mutlu, Gennady Pekhimenko, Christina Giannoula ISCA 2026 Raleigh, USA, July 1st 2026