## Slide 1
DaeMon: Architectural Support for Efficient Data Movement
in Fully Disaggregated Memory Systems
Christina Giannoula Kailong Huang, Jonathan Tang, Nectarios Koziris,
Georgios Goumas, Zeshan Chishti, Nandita Vijaykumar

## Slide 2
Executive Summary
Problem:
Efficient data movement support is a major system challenge for fully Disaggregated Systems (DSs)
Contribution:
DaeMon: the first adaptive data movement solution for fully DSs
Key Results:
DaeMon achieves 2.39x better performance and 3.06x lower data access costs over the widely-adopted scheme of moving data at page granularity
DaeMon

## Slide 3
What is resource disaggregation?
Network

## Slide 4
Monolithic vs Disaggregated Systems
`
Network
`
`
`
`
thanks to recent advances in network technologies

## Slide 5
Benefits of Fully Disaggregated Systems
Resource Utilization
Network
idle
idle
fits many jobs
Monolithic System
Disaggregated System
fits a few jobs

## Slide 6
Failure Handling
Network
Monolithic System
Disaggregated System
Benefits of Fully Disaggregated Systems

## Slide 7
Resource Scaling
Network
Benefits of Fully Disaggregated Systems

## Slide 8
Heterogeneity
Network
`
`
`
`
`
many different types of hardware devices over the network
Benefits of Fully Disaggregated Systems

## Slide 9
Resource Utilization
Failure Handling
Resource Scaling
Heterogeneity
Disaggregated systems can significantly decrease data center costs
Benefits of Fully Disaggregated Systems

## Slide 10
Baseline Disaggregated System
Network
CPU
Local
Memory
Controller
Remote
Memory
Compute
Component
Compute
Component
Compute
Component
Memory
Component
Memory
Component
Memory
Component
Memory
Component

## Slide 11
Baseline Disaggregated System
Network
CPU
Local
Memory
Controller
Remote
Memory
Compute
Component
Compute
Component
Compute
Component
Memory
Component
Memory
Component
Memory
Component
Memory
Component
hosts ~20% of application’s data

## Slide 12
Baseline Disaggregated System
Network
CPU
Local
Memory
Controller
Remote
Memory
Compute
Component
Compute
Component
Compute
Component
Memory
Component
Memory
Component
Memory
Component
Memory
Component
hosts ~80% of application’s data

## Slide 13
Baseline Disaggregated System
Network
CPU
Local
Memory
Controller
Remote
Memory
Compute
Component
Compute
Component
Compute
Component
Memory
Component
Memory
Component
Memory
Component
Memory
Component
data is typically moved at page granularity

## Slide 14
Baseline Disaggregated System
Network
CPU
Local
Memory
Controller
Remote
Memory
Compute
Component
Compute
Component
Compute
Component
Memory
Component
Memory
Component
Memory
Component
Memory
Component
distributed OS modules

## Slide 15
Why is data movement challenging?
Network
CPU
Local
Memory
Controller
Remote
Memory

## Slide 16
#1: Coarse-Grained Data Migrations
Page granularity (e.g., 4KB) data migrations:
  Software transparency
  Low metadata overheads
  High spatial locality
Network
CPU
Local
Memory
CPU
Local
Memory
Controller
Remote
Memory
Controller
Remote
Memory
high bandwidth consumption
latency-critical cache lines are slowed down

## Slide 17
#1: Coarse-Grained Data Migrations
Page granularity (e.g., 4KB) data migrations:
  Software transparency
  Low metadata overheads
  High spatial locality
Network
CPU
Local
Memory
CPU
Local
Memory
Controller
Remote
Memory
Controller
Remote
Memory
A latency-efficient and bandwidth-efficient solution is necessary

## Slide 18
#2: Non-Conventional System Design
Disaggregated systems are not monolithic
Hybrid/heterogeneous memory systems:
CPU
DRAM Cache
DRAM
System-Level
Solutions
CPU
Local
Memory
Controller
Remote
Memory
Controller
Remote
Memory
Controller
Remote
Memory
Controller
Remote
Memory
…
Thermostat [ASPLOS’17]
Kleio [HPDC’19]
Chameleon [MICRO’18]
HSCC [ICS’17]
Nimble [ASPLOS’19] …
centralized memory management
distributed memory management

## Slide 19
#2: Non-Conventional System Design
Disaggregated systems are not monolithic
Hybrid/heterogeneous memory systems:
CPU
DRAM Cache
DRAM
System-Level
Solutions
CPU
Local
Memory
Controller
Remote
Memory
Controller
Remote
Memory
Controller
Remote
Memory
Controller
Remote
Memory
…
Hardware-Level Solutions
Chop [HPCA’10]
UH-MEM [CLUSTER’17]
MemPod [HPCA’17]
LGM [IPDPS’19] …
centralized hardware units in the CPU side
would incur high hardware overheads

## Slide 20
#2: Non-Conventional System Design
Disaggregated systems are not monolithic
Hybrid/heterogeneous memory systems:
CPU
DRAM Cache
DRAM
System-Level
Solutions
CPU
Local
Memory
Controller
Remote
Memory
Controller
Remote
Memory
Controller
Remote
Memory
Controller
Remote
Memory
…
Hardware-Level Solutions
Prior solutions are not suitable or efficient
for disaggregated memory systems

## Slide 21
#3: Variability in Data Access Latencies
Data access latencies depend:
  Location of the remote memory component
CPU
Local
Memory
Controller
Remote
Memory
Controller
Remote
Memory
Controller
Remote
Memory
Controller
Remote
Memory
Controller
Remote
Memory
CPU
Local
Memory
Controller
Remote
Memory
data1
data2
different locations for application’s data

## Slide 22
#3: Variability in Data Access Latencies
Data access latencies depend:
  Location of the remote memory component
  Network contention
CPU
Local
Memory
Controller
Remote
Memory
Controller
Remote
Memory
Controller
Remote
Memory
CPU
Local
Memory
Controller
Remote
Memory
data
high contention due to concurrent jobs sharing the network

## Slide 23
#3: Variability in Data Access Latencies
CPU
Local
Memory
Controller
Remote
Memory
Controller
Remote
Memory
Controller
Remote
Memory
CPU
Local
Memory
Controller
Remote
Memory
data1
data2
CPU
Local
Memory
Controller
Remote
Memory
Controller
Remote
Memory
Controller
Remote
Memory
CPU
Local
Memory
Controller
Remote
Memory
data1
data2
data placements can vary during runtime or between multiple executions
Time
A robust solution to variability in data access latencies is necessary

## Slide 24
How can we build an efficient solution?
DaeMon
[Sigmetrics’23]

## Slide 25
1. Disaggregated Hardware Support
Network
CPU
Local
Memory
LLC
FPGA
DaeMon Compute Engine
Compute Component
Controller
Remote
Memory
DaeMon Memory Engine
Memory Component
CPU
Local
Memory
LLC
FPGA
DaeMon Compute Engine
Compute Component
Controller
Remote
Memory
DaeMon Memory Engine
Memory Component
CPU
Local
Memory
LLC
FPGA
DaeMon Compute Engine
Compute Component
Controller
Remote
Memory
DaeMon Memory Engine
Memory Component
Controller
Remote
Memory
DaeMon Memory Engine
Memory Component
dedicated units
  Independence
  High Parallelism
  High Scalability

## Slide 26
2. Multiple Granularity Data Movement
CPU
Local
Memory
LLC
Compute Component
Controller
Remote
Memory
Memory Component
Sub-block
Queue
Page
Queue
DaeMon Compute Engine
Sub-block
Queue
Page
Queue
DaeMon Memory Engine

## Slide 27
2. Multiple Granularity Data Movement
CPU
Local
Memory
LLC
Compute Component
Controller
Remote
Memory
Memory Component
Sub-block
Queue
Page
Queue
Queue Controller
DaeMon Compute Engine
Sub-block
Queue
Page
Queue
Queue Controller
DaeMon Memory Engine
Cache lines
Pages
prioritization of cache line migrations

## Slide 28
2. Multiple Granularity Data Movement
CPU
Local
Memory
LLC
Compute Component
Controller
Remote
Memory
Memory Component
Sub-block
Queue
Page
Queue
Queue Controller
DaeMon Compute Engine
Sub-block
Queue
Page
Queue
Queue Controller
DaeMon Memory Engine
Cache lines
Pages
  Software Transparency
  Low Metadata Overheads
  High Spatial Locality
  Latency-Efficiency in Critical Data

## Slide 29
3. Link Compression in Page Migrations
CPU
Local
Memory
LLC
Compute Component
Controller
Remote
Memory
Memory Component
Sub-block
Queue
Page
Queue
Queue Controller
(De) Compr. Unit
DaeMon Compute Engine
Sub-block
Queue
Page
Queue
Queue Controller
(De) Compr. Unit
DaeMon Memory Engine
Cache lines
Compressed pages
compressed pages inside the network

## Slide 30
3. Link Compression in Page Migrations
CPU
Local
Memory
LLC
Compute Component
Controller
Remote
Memory
Memory Component
Sub-block
Queue
Page
Queue
Queue Controller
(De) Compr. Unit
DaeMon Compute Engine
Sub-block
Queue
Page
Queue
Queue Controller
(De) Compr. Unit
DaeMon Memory Engine
Cache lines
Compressed pages
  Bandwidth-Efficiency
  Critical Cache Line Prioritization

## Slide 31
4. Selection Granularity Data Movement
CPU
Local
Memory
LLC
Compute Component
Controller
Remote
Memory
Memory Component
Sub-block
Queue
Page
Queue
Queue Controller
DaeMon Memory Engine
Cache lines
Pages
Sub-block
Queue
Page
Queue
Queue Controller
DaeMon Compute Engine
(De) Compr. Unit
(De) Compr. Unit
Cache line, page or both?

## Slide 32
4. Selection Granularity Data Movement
CPU
Local
Memory
LLC
Compute Component
Controller
Remote
Memory
Memory Component
Sub-block
Queue
Page
Queue
Queue Controller
DaeMon Memory Engine
Cache lines
Pages
Sub-block
Queue
Page
Queue
Queue Controller
DaeMon Compute Engine
Inflight Sub-block and Page Buffers
track pending data migrations
(De) Compr. Unit
Sub-block
Page
(De) Compr. Unit

## Slide 33
4. Selection Granularity Data Movement
CPU
Local
Memory
LLC
Compute Component
Controller
Remote
Memory
Memory Component
Sub-block
Queue
Page
Queue
Queue Controller
Selection Granularity Unit
DaeMon Compute Engine
Sub-block
Queue
Page
Queue
Queue Controller
DaeMon Memory Engine
(De) Compr. Unit
(De) Compr. Unit
Cache lines
Pages
Cache line, page or both?
Inflight Sub-block and Page Buffers
Sub-block
Page

## Slide 34
4. Selection Granularity Data Movement
CPU
Local
Memory
LLC
Compute Component
Controller
Remote
Memory
Memory Component
Sub-block
Queue
Page
Queue
Queue Controller
DaeMon Memory Engine
Cache lines
Pages
Sub-block
Queue
Page
Queue
Queue Controller
Selection Granularity Unit
DaeMon Compute Engine
Inflight Sub-block and Page Buffers
(De) Compr. Unit
(De) Compr. Unit
  Robustness
  Versatility
  Adaptivity to Runtime Changes

## Slide 35
Why does this work?
DaeMon

## Slide 36
Use Case 1: Memory Access Patterns
Controller
Remote
Memory
DaeMon Memory Engine
Memory Component
Cache lines
Compressed pages
Sub-block
Page
Time
Inflight Buffers
Utilization
Sub-block
Page
Sub-block
Page
Sub-block
Page
…
CPU
Local
Memory
LLC
DaeMon Engine
Inflight Buffers
Compute Component
high locality within pages
Selection Gran. Unit

## Slide 37
Use Case 1: Memory Access Patterns
CPU
Local
Memory
LLC
DaeMon Engine
Inflight Buffers
Compute Component
Controller
Remote
Memory
DaeMon Memory Engine
Memory Component
Cache lines
Compressed pages
Sub-block
Page
Time
Inflight Buffers
Utilization
Sub-block
Page
Sub-block
Page
Sub-block
Page
…
low locality within pages
Selection Gran. Unit

## Slide 38
Use Case 2: Network Characteristics
CPU
Local
Memory
LLC
DaeMon Engine
Inflight Buffers
Compute Component
Controller
Remote
Memory
DaeMon Memory Engine
Memory Component
Cache lines
Compressed pages
Sub-block
Page
Time
Inflight Buffers
Utilization
high bandwidth consumption
Selection Gran. Unit

## Slide 39
Use Case 2: Network Characteristics
CPU
Local
Memory
LLC
DaeMon Engine
Inflight Buffers
Compute Component
Controller
Remote
Memory
DaeMon Memory Engine
Memory Component
Cache lines
Compressed pages
Sub-block
Page
Time
Inflight Buffers
Utilization
Sub-block
Page
…
high bandwidth consumption
low bandwidth consumption
Selection Gran. Unit

## Slide 40
Use Case 3: Data Compressibility
CPU
Local
Memory
LLC
DaeMon Engine
Inflight Buffers
Compute Component
Controller
Remote
Memory
DaeMon Memory Engine
Memory Component
Cache lines
Compressed pages
Selection Gran. Unit
Sub-block
Page
Time
Inflight Buffers
Utilization
high data compressibility
app1

## Slide 41
Use Case 3: Data Compressibility
CPU
Local
Memory
LLC
DaeMon Engine
Inflight Buffers
Compute Component
Controller
Remote
Memory
DaeMon Memory Engine
Memory Component
Cache lines
Compressed pages
Selection Gran. Unit
Sub-block
Page
Time
Inflight Buffers
Utilization
high data compressibility
app1
app2
Sub-block
Page
low data compressibility

## Slide 42
Speedup in Real Applications
Chart: Workloads
| kc | tr | pr | nw | bf | bc | ts | sp | sl | hp | pf | dr | rs | GM
Page | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
ComprPage | 1.0634 | 1.3327 | 2.5092 | 4.9714 | 1.2239 | 1.2063 | 1.5945 | 1.5164 | 1.524 | 1.6679 | 1.299 | 1.0204 | 1.0076 | 1.5111
CacheLine | 0.44036 | 0.86262 | 3.8078 | 8.4073 | 0.80292 | 0.69884 | 0.71149 | 0.76462 | 0.65615 | 0.81964 | 0.46335 | 0.71766 | 0.76131 | 0.94886
CacheLine+Page | 1.0574 | 1.048 | 0.95954 | 1.0067 | 1.1436 | 1.1206 | 1.2413 | 1.1056 | 1.1065 | 1.1498 | 1.0841 | 1.1472 | 1.1581 | 1.0999
DaeMon-Compr | 1.1029 | 1.5663 | 4.7779 | 11.6554 | 1.2213 | 1.1905 | 1.426 | 1.059 | 1.0348 | 1.1213 | 1.0311 | 1.0191 | 1.0172 | 1.5347
DaeMon | 1.2037 | 1.6899 | 5.2246 | 14.5554 | 1.5595 | 1.4677 | 2.1188 | 1.619 | 1.7119 | 1.8517 | 1.3267 | 1.0793 | 1.0713 | 1.9503

## Slide 43
Speedup in Real Applications
Chart: Workloads
| kc | tr | pr | nw | bf | bc | ts | sp | sl | hp | pf | dr | rs | GM
Page | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
ComprPage | 1.0634 | 1.3327 | 2.5092 | 4.9714 | 1.2239 | 1.2063 | 1.5945 | 1.5164 | 1.524 | 1.6679 | 1.299 | 1.0204 | 1.0076 | 1.5111
CacheLine | 0.44036 | 0.86262 | 3.8078 | 8.4073 | 0.80292 | 0.69884 | 0.71149 | 0.76462 | 0.65615 | 0.81964 | 0.46335 | 0.71766 | 0.76131 | 0.94886
CacheLine+Page | 1.0574 | 1.048 | 0.95954 | 1.0067 | 1.1436 | 1.1206 | 1.2413 | 1.1056 | 1.1065 | 1.1498 | 1.0841 | 1.1472 | 1.1581 | 1.0999
DaeMon-Compr | 1.1029 | 1.5663 | 4.7779 | 11.6554 | 1.2213 | 1.1905 | 1.426 | 1.059 | 1.0348 | 1.1213 | 1.0311 | 1.0191 | 1.0172 | 1.5347
DaeMon | 1.2037 | 1.6899 | 5.2246 | 14.5554 | 1.5595 | 1.4677 | 2.1188 | 1.619 | 1.7119 | 1.8517 | 1.3267 | 1.0793 | 1.0713 | 1.9503
14.6
1.95x

## Slide 44
Speedup in Real Applications
Chart: Workloads
| kc | tr | pr | nw | bf | bc | ts | sp | sl | hp | pf | dr | rs | GM
Page | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
ComprPage | 1.0634 | 1.3327 | 2.5092 | 4.9714 | 1.2239 | 1.2063 | 1.5945 | 1.5164 | 1.524 | 1.6679 | 1.299 | 1.0204 | 1.0076 | 1.5111
CacheLine | 0.44036 | 0.86262 | 3.8078 | 8.4073 | 0.80292 | 0.69884 | 0.71149 | 0.76462 | 0.65615 | 0.81964 | 0.46335 | 0.71766 | 0.76131 | 0.94886
CacheLine+Page | 1.0574 | 1.048 | 0.95954 | 1.0067 | 1.1436 | 1.1206 | 1.2413 | 1.1056 | 1.1065 | 1.1498 | 1.0841 | 1.1472 | 1.1581 | 1.0999
DaeMon-Compr | 1.1029 | 1.5663 | 4.7779 | 11.6554 | 1.2213 | 1.1905 | 1.426 | 1.059 | 1.0348 | 1.1213 | 1.0311 | 1.0191 | 1.0172 | 1.5347
DaeMon | 1.2037 | 1.6899 | 5.2246 | 14.5554 | 1.5595 | 1.4677 | 2.1188 | 1.619 | 1.7119 | 1.8517 | 1.3267 | 1.0793 | 1.0713 | 1.9503
14.6
1.29x

## Slide 45
Speedup in Real Applications
Chart: Workloads
| kc | tr | pr | nw | bf | bc | ts | sp | sl | hp | pf | dr | rs | GM
Page | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
ComprPage | 1.0634 | 1.3327 | 2.5092 | 4.9714 | 1.2239 | 1.2063 | 1.5945 | 1.5164 | 1.524 | 1.6679 | 1.299 | 1.0204 | 1.0076 | 1.5111
CacheLine | 0.44036 | 0.86262 | 3.8078 | 8.4073 | 0.80292 | 0.69884 | 0.71149 | 0.76462 | 0.65615 | 0.81964 | 0.46335 | 0.71766 | 0.76131 | 0.94886
CacheLine+Page | 1.0574 | 1.048 | 0.95954 | 1.0067 | 1.1436 | 1.1206 | 1.2413 | 1.1056 | 1.1065 | 1.1498 | 1.0841 | 1.1472 | 1.1581 | 1.0999
DaeMon-Compr | 1.1029 | 1.5663 | 4.7779 | 11.6554 | 1.2213 | 1.1905 | 1.426 | 1.059 | 1.0348 | 1.1213 | 1.0311 | 1.0191 | 1.0172 | 1.5347
DaeMon | 1.2037 | 1.6899 | 5.2246 | 14.5554 | 1.5595 | 1.4677 | 2.1188 | 1.619 | 1.7119 | 1.8517 | 1.3267 | 1.0793 | 1.0713 | 1.9503
8.4
14.6
1.09x
0.95x
low locality within pages

## Slide 46
Speedup in Real Applications
Chart: Workloads
| kc | tr | pr | nw | bf | bc | ts | sp | sl | hp | pf | dr | rs | GM
Page | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
ComprPage | 1.0634 | 1.3327 | 2.5092 | 4.9714 | 1.2239 | 1.2063 | 1.5945 | 1.5164 | 1.524 | 1.6679 | 1.299 | 1.0204 | 1.0076 | 1.5111
CacheLine | 0.44036 | 0.86262 | 3.8078 | 8.4073 | 0.80292 | 0.69884 | 0.71149 | 0.76462 | 0.65615 | 0.81964 | 0.46335 | 0.71766 | 0.76131 | 0.94886
CacheLine+Page | 1.0574 | 1.048 | 0.95954 | 1.0067 | 1.1436 | 1.1206 | 1.2413 | 1.1056 | 1.1065 | 1.1498 | 1.0841 | 1.1472 | 1.1581 | 1.0999
DaeMon-Compr | 1.1029 | 1.5663 | 4.7779 | 11.6554 | 1.2213 | 1.1905 | 1.426 | 1.059 | 1.0348 | 1.1213 | 1.0311 | 1.0191 | 1.0172 | 1.5347
DaeMon | 1.2037 | 1.6899 | 5.2246 | 14.5554 | 1.5595 | 1.4677 | 2.1188 | 1.619 | 1.7119 | 1.8517 | 1.3267 | 1.0793 | 1.0713 | 1.9503
8.4
11.7
14.6
1.53x

## Slide 47
Speedup in Real Applications
Chart: Workloads
| kc | tr | pr | nw | bf | bc | ts | sp | sl | hp | pf | dr | rs | GM
Page | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
ComprPage | 1.0634 | 1.3327 | 2.5092 | 4.9714 | 1.2239 | 1.2063 | 1.5945 | 1.5164 | 1.524 | 1.6679 | 1.299 | 1.0204 | 1.0076 | 1.5111
CacheLine | 0.44036 | 0.86262 | 3.8078 | 8.4073 | 0.80292 | 0.69884 | 0.71149 | 0.76462 | 0.65615 | 0.81964 | 0.46335 | 0.71766 | 0.76131 | 0.94886
CacheLine+Page | 1.0574 | 1.048 | 0.95954 | 1.0067 | 1.1436 | 1.1206 | 1.2413 | 1.1056 | 1.1065 | 1.1498 | 1.0841 | 1.1472 | 1.1581 | 1.0999
DaeMon-Compr | 1.1029 | 1.5663 | 4.7779 | 11.6554 | 1.2213 | 1.1905 | 1.426 | 1.059 | 1.0348 | 1.1213 | 1.0311 | 1.0191 | 1.0172 | 1.5347
DaeMon | 1.2037 | 1.6899 | 5.2246 | 14.5554 | 1.5595 | 1.4677 | 2.1188 | 1.619 | 1.7119 | 1.8517 | 1.3267 | 1.0793 | 1.0713 | 1.9503
8.4
11.7
14.6
DaeMon performs best in real-world applications

## Slide 48
Data Access Costs in Real Applications
Chart: Data Access Costs
| kc | tr | pr | nw | bf | bc | ts | sp | sl | hp | pf | dr | rs | GM
Page | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
ComprPage | 0.67186 | 0.64218 | 0.37136 | 0.17625 | 0.68387 | 0.58995 | 0.60699 | 0.43933 | 0.58582 | 0.57144 | 0.61594 | 0.70397 | 0.72549 | 0.53847
DaeMon-Compr | 0.61237 | 0.35313 | 0.14945 | 0.12421 | 0.81743 | 0.74401 | 0.78998 | 0.87598 | 0.66665 | 0.93659 | 0.9625 | 0.69149 | 0.70649 | 0.55694
DaeMon | 0.52359 | 0.29005 | 0.13 | 0.060736 | 0.5214 | 0.49387 | 0.47504 | 0.38197 | 0.3597 | 0.48704 | 0.59716 | 0.66767 | 0.67626 | 0.37237
low locality within pages

## Slide 49
Data Access Costs in Real Applications
Chart: Data Access Costs
| kc | tr | pr | nw | bf | bc | ts | sp | sl | hp | pf | dr | rs | GM
Page | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
ComprPage | 0.67186 | 0.64218 | 0.37136 | 0.17625 | 0.68387 | 0.58995 | 0.60699 | 0.43933 | 0.58582 | 0.57144 | 0.61594 | 0.70397 | 0.72549 | 0.53847
DaeMon-Compr | 0.61237 | 0.35313 | 0.14945 | 0.12421 | 0.81743 | 0.74401 | 0.78998 | 0.87598 | 0.66665 | 0.93659 | 0.9625 | 0.69149 | 0.70649 | 0.55694
DaeMon | 0.52359 | 0.29005 | 0.13 | 0.060736 | 0.5214 | 0.49387 | 0.47504 | 0.38197 | 0.3597 | 0.48704 | 0.59716 | 0.66767 | 0.67626 | 0.37237
medium locality within pages

## Slide 50
Data Access Costs in Real Applications
Chart: Data Access Costs
| kc | tr | pr | nw | bf | bc | ts | sp | sl | hp | pf | dr | rs | GM
Page | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
ComprPage | 0.67186 | 0.64218 | 0.37136 | 0.17625 | 0.68387 | 0.58995 | 0.60699 | 0.43933 | 0.58582 | 0.57144 | 0.61594 | 0.70397 | 0.72549 | 0.53847
DaeMon-Compr | 0.61237 | 0.35313 | 0.14945 | 0.12421 | 0.81743 | 0.74401 | 0.78998 | 0.87598 | 0.66665 | 0.93659 | 0.9625 | 0.69149 | 0.70649 | 0.55694
DaeMon | 0.52359 | 0.29005 | 0.13 | 0.060736 | 0.5214 | 0.49387 | 0.47504 | 0.38197 | 0.3597 | 0.48704 | 0.59716 | 0.66767 | 0.67626 | 0.37237
high locality within pages

## Slide 51
Data Access Costs in Real Applications
Chart: Workloads
| kc | tr | pr | nw | bf | bc | ts | sp | sl | hp | pf | dr | rs | GM
Page | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
ComprPage | 0.67186 | 0.64218 | 0.37136 | 0.17625 | 0.68387 | 0.58995 | 0.60699 | 0.43933 | 0.58582 | 0.57144 | 0.61594 | 0.70397 | 0.72549 | 0.53847
DaeMon-Compr | 0.61237 | 0.35313 | 0.14945 | 0.12421 | 0.81743 | 0.74401 | 0.78998 | 0.87598 | 0.66665 | 0.93659 | 0.9625 | 0.69149 | 0.70649 | 0.55694
DaeMon | 0.52359 | 0.29005 | 0.13 | 0.060736 | 0.5214 | 0.49387 | 0.47504 | 0.38197 | 0.3597 | 0.48704 | 0.59716 | 0.66767 | 0.67626 | 0.37237
3.06x
DaeMon significantly reduces data access costs in real-world applications

## Slide 52
Speedup in Many Memory Components
Chart: #Memory Components
| 1 | 2 | 4 | 1 | 2 | 4 | 1 | 2 | 4 | 1 | 2 | 4
Page | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
DeaMon | 23.5914 | 15.1326 | 14.9332 | 2.6648 | 2.4973 | 2.4309 | 2.0329 | 1.7803 | 1.7024 | 1.0749 | 1.0843 | 1.0847
23.6
15.1
14.9
nw
ts
sp
dr
3.25x
DaeMon constitutes a scalable solution

## Slide 53
Speedup in Multiple Co-Running Jobs
DaeMon over Page
Chart: Workloads
| bf-dr-ts-nw | bf-dr-ts-sp | pr-dr-sp-nw | pr-nw-ts-sp | bc-dr-ts-sp | tr-dr-ts-sp | bc-nw-ts-sp | tr-nw-ts-sp | dr-ts-sp-nw
Core 1 | 3.2575 | 1.1839 | 1.5857 | 2.1285 | 1.3363 | 1.3474 | 2.4161 | 4.478 | 2.3418
Core 2 | 3.1278 | 1.1236 | 3.2612 | 3.8505 | 1.309 | 1.1629 | 2.6351 | 5.7688 | 5.3965
Core 3 | 5.0092 | 1.8679 | 2.8412 | 7.1298 | 1.9351 | 2.2901 | 4.1087 | 6.5931 | 2.5067
Core 4 | 3.2816 | 1.1839 | 5.7805 | 2.6804 | 1.3564 | 1.2795 | 2.635 | 4.8641 | 2.5041
DaeMon constitutes a versatile solution
1.96x

## Slide 54
Conclusion
Data movement is a major challenge for fully DSs
Prior solutions are not suitable or efficient
DaeMon is the first adaptive data movement solution
DaeMon consists of four techniques:
  Disaggregated hardware support
  Decoupled multiple granularity data movement
  Link compression in page movements
  Selection granularity data movement
DaeMon’s benefits over the widely-adopted scheme:
  2.39x better performance
  3.06x lower data access
DaeMon is highly-efficient, low-cost, scalable and robust
DaeMon

## Slide 55
DaeMon: Architectural Support for Efficient Data Movement
in Fully Disaggregated Memory Systems
Christina Giannoula Kailong Huang, Jonathan Tang, Nectarios Koziris,
Georgios Goumas, Zeshan Chishti, Nandita Vijaykumar
Thank you!