## Slide 1
PyGim: An Efficient Graph Neural Network Library for Real Processing-In-Memory Architectures
Christina Giannoula, Peiming Yang, Ivan Fernandez, Jiacheng Yang, Sankeerth Durvasula, Yu Xin Li, Mohammad Sadrosadati, Juan Gomez Luna, Onur Mutlu, Gennady Pekhimenko

## Slide 2
Key Results: PyGim improves (i) performance and energy efficiency by 3.7× and 2.3× over state-of-the-art schemes, and (ii) core utilization on PIM system by 11.6× over PyTorch on GPUs
Executive Summary
Problem: The memory-intensive kernels of Graph Neural Networks (GNNs) dominate execution time (~91%) and are significantly bottlenecked by memory bandwidth in procesor-centric systems (CPUs/GPUs)
PyGim: An efficient and easy-to-use GNN library for real Processing-In-Memory (PIM) systems
Key Ideas & Benefits:
Cost Effectiveness: Heteregenous GNN kernels are executed in the best-fit hardware
High Performance: (i) Enabling three levels of parallelism with various strategies in the PIM side and (ii) adapting best-performing parallelization strategy to the graph’s unique characteristics
High Programming Ease: (i) Providing a handy Python API and (ii) automatically tuning the best-fit parallelization strategy without programmer intervention
github.com/CMU-SAFARI/PyGim
Motivation: PIM provide significantly high memory bandwidth by enabling computation to be performed close to the application data

## Slide 3
Talk Outline
Background & Motivation
PyGim Design
Evaluation

## Slide 4
GNNs Are Widely Used in Real-World Applications
GNNs are state-of-the-art ML models for analyzing graph-structure data
GNNs have a lot of applications:
Drug Discovery
Recommendation Systems
Fraud Detection

## Slide 5
Execution Steps of GNN Layers
GNNs comprise a few layers (e.g., 3-5 layers)
1
2
5
4
6
Adjacency (Sparse) Matrix
Input Feature

## Slide 6
Input Feature
Execution Steps of GNN Layers
GNNs comprise a few layers (e.g., 3-5 layers)
Input Feature
1
2
5
4
6
Adjacency (Sparse) Matrix
1
2
5
4
6

## Slide 7
Execution Steps of GNN Layers
GNNs comprise a few layers (e.g., 3-5 layers)
1
2
5
4
6
Adjacency (Sparse) Matrix
Input Feature
1
2
5
4
6
1
2
5
4
6
Output Feature
Aggregation Result
Neural Network (NN)

## Slide 8
Execution Steps of GNN Layers
GNNs comprise a few layers (e.g., 3-5 layers)
Each GNN layer has two execution steps:
Aggregation
Combination
Aggregate neighbor’s feature, corresponds to Sparse Matrix Matrix Multiplication (SpMM)
Combine features by NN. Typically comprises compute-intensive kernels (e.g., GEMMs)
1
2
5
4
6
Adjacency (Sparse) Matrix
Input Feature
Neural Network (NN)
1
2
5
4
6
1
2
5
4
6
Output Feature
Aggregation Result

## Slide 9
GNN Aggregation Is Memory-Bandwidth-Bound In GPUs
Using a RTX 3090 GPU with ~900 GB/s bandwidth, we find that GNN Aggregation
takes ~91% of the inference time
achieves less than 2% core utilization
Roofline Analysis
Bandwidth-Bound

## Slide 10
PIM Alleviates The Data Movement Bottleneck
Near-bank PIM: each PIM core is tightly coupled with one (or a few) DRAM banks
Near-bank PIM cores have significantly higher memory bandwidth than Host cores
A Near-Bank PIM System
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host Processor
(e.g., CPU/GPU)
Host Cores
Shared Cache
Bus
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
Standard Memory Modules
Bus
PIM Provides A Promising Solution for GNN Aggregation

## Slide 11
Talk Outline
Background & Motivation
PyGim Design
Evaluation

## Slide 12
PyGim Overview
An efficient and easy-to-use GNN library for real PIM systems
PyGim incorporates 4 key components:
Cooperative Acceleration (CoA)
Parallelism Fusion (PaF)
Lightweight Tuning
Handy Programming Interface
Run heterogeneous kernels in the best-fit hardware
Strives a balance between computation and data transfer
Automatically tunes the best-performing PaF strategy
Integrates a handy Python (PyTorch) API
Parallelism Fusion (PaF)
Lightweight Tuning
Handy Programming Interface
Strives a balance between computation and data transfer
Automatically tunes the best-performing PaF strategy
Integrates a handy Python (PyTorch) API

## Slide 13
1. Cooperative Acceleration (CoA)
Heterogeneous kernels are running in the best-fit underlying hardware
Combination runs on Host cores
Aggregation runs on PIM cores
A Near-Bank PIM System
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host Processor
(e.g., CPU/GPU)
Host Cores
Shared Cache
Bus
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
Standard Memory Modules
Bus
GNN Aggregation
GNN Combination

## Slide 14
PyGim Overview
An efficient and easy-to-use GNN library for real PIM systems
PyGim incorporates 4 key components:
Lightweight Tuning
Handy Programming Interface
Expensive Data Transfer Costs
challenge
Cooperative Acceleration (CoA)
Parallelism Fusion (PaF)

## Slide 15
Challenge 1: Expensive Data Transfer Costs
Alleviate the overheads of passing the output data of the one step as input data to the next step
A Near-Bank PIM System
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host Processor
(e.g., CPU/GPU)
Host Cores
Shared Cache
Bus
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
Standard Memory Modules
Bus
GNN Aggregation
GNN Combination
data

## Slide 16
PyGim Overview
An efficient and easy-to-use GNN library for real PIM systems
PyGim incorporates 4 key components:
Cooperative Acceleration (CoA)
Parallelism Fusion (PaF)
Lightweight Tuning
Handy Programming Interface
Expensive Data Transfer Costs
challenge
solution

## Slide 17
2. Parallelism Fusion (PaF)
PaF (i) strives a balance between computation and data transfer costs and (ii) efficiently covers various real-world graphs that exhibit diverse characteristics
PaF enablers 3 levels of parallelism:
  Across PIM Clusters: Edge- + Feature-level parallelism
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1
Cluster 2
Cluster 3
Cluster 4
Across PIM Clusters

## Slide 18
2. Parallelism Fusion (PaF)
PaF (i) strives a balance between computation and data transfer costs and (ii) efficiently covers various real-world graphs that exhibit diverse characteristics
PaF enablers 3 levels of parallelism:
  Across PIM Clusters: Edge- + Feature-level parallelism
  Within PIM Cluster: Vertex-/Edge-level parallelism
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1
Cluster 2
Cluster 3
Cluster 4
Across PIM Clusters
Within PIM Cluster

## Slide 19
2. Parallelism Fusion (PaF)
PaF (i) strives a balance between computation and data transfer costs and (ii) efficiently covers various real-world graphs that exhibit diverse characteristics
PaF enablers 3 levels of parallelism:
  Across PIM Clusters: Edge- + Feature-level parallelism
  Within PIM Cluster: Vertex-/Edge-level parallelism
  Within PIM Core: Vertex-/Edge-level parallelism
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1
Cluster 2
Cluster 3
Cluster 4
Across PIM Clusters
Within PIM Cluster
PIM Core
Threads
Within PIM Core

## Slide 20
2. Parallelism Fusion (PaF)
PaF (i) strives a balance between computation and data transfer costs and (ii) efficiently covers various real-world graphs that exhibit diverse characteristics
PaF enablers 3 levels of parallelism:
  Across PIM Clusters: Edge- + Feature-level parallelism
  Within PIM Cluster: Vertex-/Edge-level parallelism
  Within PIM Core: Vertex-/Edge-level parallelism
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1
Cluster 2
Cluster 3
Cluster 4
Across PIM Clusters
Within PIM Cluster
PIM Core
Threads
Within PIM Core
Reduces data transfer costs
Reduce computation costs

## Slide 21
An Aggregation Example
E.g., a graph with 8 vertices and 14 edges
  SpMM is used for aggregation
1
2
3
4
5
8
6
7
SpMM
Adjacency (Sparse) Matrix
Input Feature Matrix
Aggregation Results
1
2
3
4
5
8
6
7

## Slide 22
2.1 PaF Parallelism Across PIM Clusters
PaF (i) strives a balance between computation and data transfer costs and
(ii) covers various graphs with diverse characteristics
PaF enables 3 levels of parallelism:
  Across PIM Clusters: Edge- and Feature-level parallelism
  Within PIM Cluster: Vertex- or Edge-level parallelism
  Within PIM Core: Vertex- or Edge-level parallelism
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1
Cluster 2
Cluster 3
Cluster 4
Across PIM Clusters
4 PIM Clusters

## Slide 23
Across PIM Clusters: Edge- & Feature-Level Parallelism
E.g., creating 4 PIM clusters with 2 Edge partitions and 2 Feature partitions
Adjacency (Sparse) Matrix
Input Feature Matrix
1
2
3
4
5
8
6
7
Edge-level partition
Clusters 1,2
Clusters 3,4
Clusters 1,2
Clusters 3,4

## Slide 24
Across PIM Clusters: Edge- & Feature-Level Parallelism
E.g., creating 4 PIM clusters with 2 Edge partitions and 2 Feature partitions
Adjacency (Sparse) Matrix
Input Feature Matrix
1
2
3
4
5
8
6
7
Clusters 1,2
1
2
3
4
5
8
6
7
Clusters 3,4
Edge-level partition
Feature-level partition
Clusters 1,2
Clusters 3,4
Cluster
1
Cluster
3
Cluster
4
Cluster
2
Clusters 1,2
Clusters 3,4

## Slide 25
Across PIM Clusters: Edge- & Feature-Level Parallelism
E.g., creating 4 PIM clusters with 2 Edge partitions and 2 Feature partitions
Adjacency (Sparse) Matrix
Input Feature Matrix
Partial Results for Output
Cluster 1
Cluster 3
Cluster 2
Cluster 4
1
2
3
4
5
8
6
7
Cluster 1
1
2
3
4
5
8
6
7
Cluster 2
1
2
3
4
5
8
6
7
Cluster 3
1
2
3
4
5
8
6
7
Cluster 4
Edge-level partition
Feature-level partition
Clusters 1,2
Clusters 3,4
Cluster
1
Cluster
3
Cluster
4
Cluster
2
Merged by Host cores

## Slide 26
Across PIM Clusters: Edge- & Feature-Level Parallelism
E.g., creating 4 PIM clusters with 2 Edge partitions and 2 Feature partitions
Adjacency (Sparse) Matrix
Input Feature Matrix
Partial Results for Output
Cluster 1
Cluster 3
Cluster 2
Cluster 4
1
2
3
4
5
8
6
7
Cluster 1
1
2
3
4
5
8
6
7
Cluster 2
1
2
3
4
5
8
6
7
Cluster 3
1
2
3
4
5
8
6
7
Cluster 4
Edge-level partition
Feature-level partition
Clusters 1,2
Clusters 3,4
Cluster
1
Cluster
3
Cluster
4
Cluster
2
Merged by Host cores
Aggregation Results

## Slide 27
2.2 PaF Parallelism Within PIM Cluster
PaF (i) strives a balance between computation and data transfer costs and
(ii) covers various graphs with diverse characteristics
PaF enables 3 levels of parallelism:
  Across PIM Clusters: Edge- and Feature-level parallelism
  Within PIM Cluster: Vertex- or Edge-level parallelism
  Within PIM Core: Vertex- or Edge-level parallelism
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1
Cluster 2
Cluster 3
Cluster 4
Within PIM Cluster
Clusters 3,4
Cluster
4

## Slide 28
Within a PIM Cluster: Vertex- or Edge-Level Parallelism
E.g., balancing vertices or balancing edges across PIM cores within the cluster
Adjacency (Sparse) Matrix
Core 1
Balance Vertices Across PIM Cores
Balance Edges Across PIM Cores
Adjacency (Sparse) Matrix
Core 2
Core 1
Core 2
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1 has 2 PIM Cores
Cluster 2

## Slide 29
2.3 PaF Parallelism Within PIM Core
PaF (i) strives a balance between computation and data transfer costs and
(ii) covers various graphs with diverse characteristics
PaF enables 3 levels of parallelism:
  Across PIM Clusters: Edge- and Feature-level parallelism
  Within PIM Cluster: Vertex- or Edge-level parallelism
  Within PIM Core: Vertex- or Edge-level parallelism
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1
Cluster 2
Cluster 3
Cluster 4
PIM Core
Threads
Within PIM Core
PIM Core

## Slide 30
Within a PIM Core: Vertex- or Edge-Level Parallelism
E.g., balancing vertices or balancing edges across threads within a PIM core
Adjacency (Sparse) Matrix
Thread 1
Balance Vertices Across Threads
Balance Edges Across Threads
Adjacency (Sparse) Matrix
PIM Core
Threads
PIM Core supports 4 threads
Thread 2
Thread 3
Thread 4
Thread 1
Thread 2
Thread 3
Thread 4
Synchronization is implement
with lock-free or fine-grained locking schemes

## Slide 31
PyGim Overview
An efficient and easy-to-use GNN library for real PIM systems
PyGim incorporates 4 key components:
Cooperative Acceleration (CoA)
Parallelism Fusion (PaF)
Lightweight Tuning
Handy Programming Interface
Expensive Data Transfer Costs
Programmability in
Real-World Graphs
challenge
How many edge partitions across clusters?
How many feature partitions across clusters?
Balance vertices or edges within PIM cluster?
Balance vertices or edges within PIM core?

## Slide 32
PaF supports a wide variety of parallelization strategies:
  Typically there is no one-size-fits-all solution
Challenge = manually tuning the parallelization strategy poses significant burdens for developers
  Unique graph's characteristics need different tuning
Challenge 2: Programmability in Real-World Graphs
Real-world graphs exhibit diverse characteristics
regular graph
power-law graph
diagonal graph

## Slide 33
PyGim Overview
An efficient and easy-to-use GNN library for real PIM systems
PyGim incorporates 4 key components:
Cooperative Acceleration (CoA)
Parallelism Fusion (PaF)
Lightweight Tuning
Handy Programming Interface
Expensive Data Transfer Costs
Programmability in
Real-World Graphs
challenge
solution
Notes: - To solve this, we design a lightweight tuner.

## Slide 34
PyGim Tuner predicts the best-performing PaF strategy without manual programmer intervention
  Hardware profiler generate a group of performance measurements
  Performance predictor predict the execution of potential PaF strategy
  PaF selector apply the best-performing PaF strategy
3. Lightweight Tuning
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Real PIM System
Real-world Graph
Best-performing
PaF Strategy
Tunes
PyGim Tuner
PaF Selector
Performance Predictor
Host->PIM
PIM->Host
PIM Kernel
Host Kernel
Hardware Profiler
PaF Generator

## Slide 35
PyGim Overview
An efficient and easy-to-use GNN library for real PIM systems
PyGim incorporates 4 key components:
Cooperative Acceleration (CoA)
Parallelism Fusion (PaF)
Lightweight Tuning
Handy Programming Interface

## Slide 36
PyGim integrates a handy Python API (currently integrated with PyTorch)
4. Handy Programming Interface
import torch, pygim as gyn
class GCNConv(torch.nn.Module):
def __init__(self, hidden_size):
self.linear = torch.nn.Linear(feature_size, features_size)
def forward(self, graph_pim, in_dense):
# Execute memory-intensive operator in PIM devices
dense_parts = col_split(in_dense)
out_dense = gyn.pim_run_aggr(graph_pim, dense_parts)
# Execute compute-intensive operator in Host (e.g., CPU/GPU)
out = self.linear(out_dense)
return out
gyn.pim_init_devices(num_pim_devices) # Initialize PIM devices
data = load_dataset() # Load graph
# Tune the PaF strategy
graph_parts, config = gyn.tune(data.graph, feature_size, device_info)
graph_pim = gyn.load_graph_pim(graph_parts) # Partition graph to PIM
# Create GNN model
model = torch.nn.Sequential([Linear(in_channels, feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
Linear(feature_size, out_channels)])
model.forward(graph_pim, data.features) # GCN inference
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
# Create GNN model model=torch.nn.Sequential([Linear(in_channels,feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
Linear(feature_size, out_channels)])
import … pygim as gyn
out_dense = gyn.pim_run_aggr(graph_pim, dense_parts)
# Execute memory-intensive kernel in real PIM devices
graph_pim= gyn.tune(data.graph, feature_size, device_info)
# Tune the PaF strategy

## Slide 37
Deploy Your GNNs Effortlessly with PyGim and Enjoy the PIM Benefits!
import torch, pygim as gyn
class GCNConv(torch.nn.Module):
def __init__(self, hidden_size):
self.linear = torch.nn.Linear(feature_size, features_size)
def forward(self, graph_pim, in_dense):
# Execute memory-intensive operator in PIM devices
dense_parts = col_split(in_dense)
out_dense = gyn.pim_run_aggr(graph_pim, dense_parts)
# Execute compute-intensive operator in Host (e.g., CPU/GPU)
out = self.linear(out_dense)
return out
gyn.pim_init_devices(num_pim_devices) # Initialize PIM devices
data = load_dataset() # Load graph
# Tune the PaF strategy
graph_parts, config = gyn.tune(data.graph, feature_size, device_info)
graph_pim = gyn.load_graph_pim(graph_parts) # Partition graph to PIM
# Create GNN model
model = torch.nn.Sequential([Linear(in_channels, feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
Linear(feature_size, out_channels)])
model.forward(graph_pim, data.features) # GCN inference
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
# Create GNN model model=torch.nn.Sequential([Linear(in_channels,feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
Linear(feature_size, out_channels)])
import … pygim as gyn
out_dense = gyn.pim_run_aggr(graph_pim, dense_parts)
# Execute memory-intensive kernel in real PIM devices
graph_pim= gyn.tune(data.graph, feature_size, device_info)
# Tune the PaF strategy
UPMEM PIM
fast-forwarded
Memory
small cores
Computation is performed inside real PIM devices!

## Slide 38
Talk Outline
Background & Motivation
PyGim Design
Evaluation

## Slide 39
Evaluation Methodology
UPMEM PIM server: 16 PIM DIMMs with 1992 PIM Cores (24 threads per core) in total
GNN models: GCN, GIN, SAGE
Datasets: ogbn-proteins, reddit, amazonProducts
Comparison points:
  PyTorch running on host CPU
  SparseP [Sigmetrics’22] (2×) running SpMM as multiple SpMV kernels on PIM cores
  GraNDe [IEEE Trans. Comput.’23]: optimizes GNN aggregation on near-rank PIM systems
UPMEM PIM System
PIM-Enabled Memory
PIM-Enabled Memory
124 GB PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host CPU (2-socket Intel Xeon)
Host Cores
Shared Cache
Bus
PIM-Enabled Memory
PIM-Enabled Memory
128 GB Main Memory
Bus

## Slide 40
Performance Evaluation in GNN Inference
Chart: INT32
| GIN | GCN | SAGE | GIN | GCN | SAGE | GIN | GCN | SAGE
PyTorch (CPU) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SparseP1 | 1.104 | 1.3051 | 1.2104 | 1.3998 | 1.347 | 1.341 | 1.143 | 1.1836 | 1.217
SparseP2 | 1.0987 | 1.2522 | 1.1822 | 1.3804 | 1.319 | 1.2894 | 1.1353 | 1.162 | 1.1845
GraNDe | 0.47434 | 0.53453 | 0.50797 | 0.56132 | 0.51479 | 0.52287 | 0.40931 | 0.4062 | 0.42852
PyGim_CSR | 2.7667 | 3.2756 | 3.0324 | 3.3892 | 3.4308 | 3.3225 | 2.6124 | 2.8215 | 2.9016
PyGim_COO | 2.6776 | 3.3551 | 3.0108 | 3.4015 | 3.4393 | 3.3107 | 2.6037 | 2.8016 | 2.6584
ogbn-proteins
reddit
amazonProducts

## Slide 41
Performance Evaluation in GNN Inference
Chart: INT32
| GIN | GCN | SAGE | GIN | GCN | SAGE | GIN | GCN | SAGE
PyTorch (CPU) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SparseP1 | 1.104 | 1.3051 | 1.2104 | 1.3998 | 1.347 | 1.341 | 1.143 | 1.1836 | 1.217
SparseP2 | 1.0987 | 1.2522 | 1.1822 | 1.3804 | 1.319 | 1.2894 | 1.1353 | 1.162 | 1.1845
GraNDe | 0.47434 | 0.53453 | 0.50797 | 0.56132 | 0.51479 | 0.52287 | 0.40931 | 0.4062 | 0.42852
PyGim_CSR | 2.7667 | 3.2756 | 3.0324 | 3.3892 | 3.4308 | 3.3225 | 2.6124 | 2.8215 | 2.9016
PyGim_COO | 2.6776 | 3.3551 | 3.0108 | 3.4015 | 3.4393 | 3.3107 | 2.6037 | 2.8016 | 2.6584
ogbn-proteins
reddit
amazonProducts
PyGim significantly outperforms PyTorch (CPU) and prior PIM-based schemes by 3.1× and 4.4×, respectively

## Slide 42
Energy Efficiency Evaluation in GNN Inference
Chart: INT32
| GIN | GCN | SAGE | GIN | GCN | SAGE | GIN | GCN | SAGE
PyTorch (CPU) | 2564.2726 | 2587.1552 | 2442.4522 | 4433.7424 | 4279.762 | 4359.3713 | 5852.4966 | 5620.9367 | 5704.5425
SparseP1 | 4946.4061 | 4897.4054 | 4944.507 | 7214.2204 | 7086.3536 | 7154.5176 | 10135.5761 | 9977.7677 | 10039.4813
SparseP2 | 4487.6501 | 4451.2338 | 4496.3087 | 6478.7246 | 6381.0069 | 6422.2122 | 9143.2736 | 9046.1845 | 9065.546
GraNDe | 6149.8183 | 5918.9864 | 6105.7194 | 8200.6406 | 7889.4481 | 7882.9551 | 13149.1481 | 13064.0146 | 13328.4552
PyGim_CSR | 1856.5666 | 1765.8154 | 1798.3173 | 2555.2897 | 2450.003 | 2473.5083 | 3737.752 | 3570.6333 | 3628.2915
PyGim_COO | 1912.043 | 1882.2876 | 1899.8371 | 2572.9546 | 2496.2467 | 2576.2211 | 3735.719 | 3580.2291 | 3671.5764
ogbn-proteins
reddit
amazonProducts
PyGim improves energy efficiency by 2.7× and 3.3× compared to PyTorch (CPU) and prior PIM-based schemes, respectively

## Slide 43
Scalability Analysis of PyGim in the Aggregation Kernel
PyGim is scalable: when we double the number of PIM devices, performance improves by 1.4× on average
Chart: INT32 (fixed PaF configuration)
| ogbn-proteins | reddit
8 PIM devices | 2268.771 | 3398.055
16 PIM devices | 1621.8329 | 2392.148
32 PIM devices | 1411.6189 | 2144.128

## Slide 44
Performance of PaF Configurations in Aggregation for Various Graphs
Chart: INT32 (fixed 32 PIM devices)
| ogbn-proteins | reddit
1-32-1 | 968.1649 | 1485.717
1-64-2 | 1393.6189 | 2144.127
2-16-1 | 1028.329 | 1277.1429
2-32-2 | 1232.9782 | 1667.419
4-8-1 | 1197.6889 | 1279.854
4-16-2 | 1246.2359 | 1460.617
No one-size-fits-all: the graph’s characteristics affect the best-performing parallelization strategy
Triple of values = PaF configuration for #edge partitions, #feature partitions and #PIM clusters per device

## Slide 45
Performance of PaF Configurations in Aggregation for Various Graphs
Chart: INT32 (fixed 32 PIM devices)
| ogbn-proteins | reddit
1-32-1 | 968.1649 | 1485.717
1-64-2 | 1393.6189 | 2144.127
2-16-1 | 1028.329 | 1277.1429
2-32-2 | 1232.9782 | 1667.419
4-8-1 | 1197.6889 | 1279.854
4-16-2 | 1246.2359 | 1460.617
Triple of values = PaF configuration for #edge partitions, #feature partitions and #PIM clusters per device
Commodity DRAM has multiple hierarchy levels (e.g., DIMM-, rank-, bank-group-, bank-level), each level has different characteristics. PIM architects can enable different hardware optimizations at each level of hierarchy. Then, software engineers can design different software optimization techniques for each different level of hardware hierarchy to enable high performance in PIM executions via hardware software co-design.
Recommendation 1
The system performance of sparse workloads highly depends on the particular patterns of each input. Systems software engineers can design various optimizations strategies to effectively support diverse inputs. They can then develop tuning mechanisms (e.g., intelligent heuristics, prediction models, compilers, automation tools) to automatically adjust these strategies based on the input, with minimal programming effort, thus achieving the highest possible performance in PIM systems.
Recommendation 2

## Slide 46
Characteristics of CPU, PIM and GPU Systems
System | INT32 Peak Performance | FP32 Peak Performance | Total Bandwidth | Technology Node
CPU Xeon 4215 | 0.64 TOPS | 1.28 TFLOPS | 23.1 GB/s | 14nm
UPMEM PIM | 0.12 TOPS | 0.025 TFLOPS | 1390 GB/s | at least 20nm
GPU GTX 1080 Ti | 13.25 TOPS | 13.25 TFLOPS | 359.9 GB/s | 16nm
GPU RTX 2080 Ti | 16.94 TOPS | 16.94 TFLOPS | 558.1 GB/s | 12nm
GPU RTX 3090 | 17.79 TOPS | 35.58 TFLOPS | 936.2 GB/s | 8nm
Across last GPU generations:
memory bandwidth has tripled (~3×)
(last two generations) compute throughput has been doubled (~2×)

## Slide 47
Core Utilization in GNN Aggregation
Dataset & data type/ Software library | Reddit INT32 | Reddit FP32
Intel MKL (CPU Intel Xeon 4215) | 0.63% | 0.22%
CUDA (GPU GTX 1080 Ti) | 0.62% | 0.62%
CUDA (GPU RTX 2080 Ti) | 0.68% | 0.67%
CUDA (GPU RTX 3090) | 1.56% | 0.78%
PyGim (UPMEM PIM) | 13.86% | 9.13%
Core utilization in GNN aggregation remains similarly low across GPU generations
PyGim running on a real PIM system achieves
significantly higher core utilization (11.6x on average) than the PyTorch on GPUs

## Slide 48
More in the Paper
Analysis within a PIM core
Analysis within a PIM cluster
Analysis across PIM clusters
PyGim tuning efficiency
Scalability analysis
Analysis on different data types
Analysis on different compression formats
Performance evaluation in GNN training
Recommendations
https://arxiv.org/pdf/2402.16731

## Slide 49
PyGim is Open Source
github.com/CMU-SAFARI/PyGim
PyGim

## Slide 50
Conclusion
We present PyGim, a handy ML library that significantly improves performance, energy efficiency and cost effectiveness in GNNs through real PIM devices
Key Ideas & Benefits:
balances computation and data transfer costs via configurable parallelization strategies for diverse real-world graphs
automatically tunes the best-fit strategy without programmer intervention
Key Results:
performance and energy efficiency by 3.7× and 2.3× over SOTA schemes
core utilization on PIM system by 11.6× over PyTorch on GPUs
PyGim

## Slide 51
PyGim: An Efficient Graph Neural Network Library for Real Processing-In-Memory Architectures
Christina Giannoula,
Peiming Yang, Ivan Fernandez, Jiacheng Yang, Sankeerth Durvasula, Yu Xin Li, Mohammad Sadrosadati, Juan Gomez Luna, Onur Mutlu, Gennady Pekhimenko