## Slide 1
SMASH: Co-Designing Software Compression
and Hardware-Accelerated Indexing
for Efficient Sparse Matrix Operations
1: Summary
2: Sparse Matrix Operations and Compression Formats
3: SMASH
4: Software Compression Scheme
5: Hardware Acceleration Unit
8: Evaluation
Hardware Overhead
Other Results in the Paper
Konstantinos Kanellopoulos Nandita Vijaykumar Christina Giannoula
Roknoddin Azizi Skanda Koppula Nika Mansouri Ghiasi
Taha Shahroodi Juan Gomez Luna Onur Mutlu
Many important workloads heavily involve Sparse Matrix Operations
Shortcomings of existing compression formats
  expensive discovery of the positions of non-zero elements or
  narrow applicability
SMASH: hardware/software cooperative mechanism for
efficient sparse matrix storage and computation
  Software: Efficient compression scheme using
  a Hierarchy of Bitmaps
  Hardware: Hardware unit interprets the Bitmap Hierarchy
  and accelerates indexing
Performance improvement: 38% and 44% for SpMV and SpMM
over the widely used CSR format
SMASH is highly efficient, low-cost and widely applicable
General formats optimize for storage
Specialized formats assume
specific matrix structures
and patterns (e.g., diagonals)
Expensive discovery of the positions of non-zero elements
Narrow
applicability
1
2
0
row_ptr
col_ind
values
5
0
0
0
0
0
3
4
0
8
0
0
0
0
0
3
Α =
MATRIX
CSR
Compressed Sparse Row
Indexing overhead
Requires multiple data-dependent
memory accesses
1
3
4
5
0
2
3
1
3
5
3
4
8
3
Efficient compression using a Hierarchy of Bitmaps
Software
Unit that scans bitmaps to accelerate indexing
Hardware
SMASH
ISA
Hardware/Software cooperative mechanism: Explain SMASH
Enables highly-efficient sparse matrix compression and computation
General across a diverse set of sparse matrices and sparse matrix operations
Encodes the presence/absence of a non-zero element
in a block of the original matrix with a single bit
Bitmap
SRAM BUFFER 2
SRAM BUFFER 1
SRAM BUFFER 0
Matrix Parameters
Bitmap Parameters
Hardware Logic
NON ZERO INDEX
SCAN
READ
UPDATE
Group 3
BITMAP
BUFFERS
CPU
SMASH ISA
Bitmap Management Unit (BMU)
NON-ZERO VALUES ARRAY
NZ
Z
Z
Z
NZ
NZ
Z
Z
Z
Z
Z
Z
Z
Z
Z
Z
Bitmap 0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
0
0
1
1
1
Bitmap 1
Bitmap 2
Compression Ratio 4:1
Compression Ratio 2:1
MATRIX
NZ
NZ
NZ
Hierarchy of Bitmaps
Group 2
Simulator: ZSim Simulator
Workloads:
    Sparse Matrix Kernels
SpMV & SpMM from TACO
    Graph Applications
  PageRank & Betweenness Centrality
  from Ligra
Input dataset:
  15 diverse sparse matrices & 4 graphs
  from the Sparse Suite Collection [4]
  Sparsity ranges from 0.01% to 8.79%
Methodology
Performance Improvement using SMASH
SMASH provides significant performance improvements over state-of-the-art formats
Chart: Speedup over TACO-CSR
| SpMV | SpMM | PageRank | BC
TACO-CSR | 1 | 1 | 1 | 1
TACO-BCSR | 1.04 | 1.1 | 1.19 | 1.26
SMASH | 1.38 | 1.44 | 1.27 | 1.31
Number of Executed Instructions
SMASH significantly reduces
the number of executed instructions
Chart: Normalized Number of Instructions over TACO-CSR
| SpMV | SpMM | PageRank | BC
TACO-CSR | 1 | 1 | 1 | 1
TACO-BCSR | 0.89 | 0.81 | 0.82 | 0.78
SMASH | 0.63 | 0.54 | 0.75 | 0.7
Chart: INCREASING SPARSITY 
| M1 | M2 | M3 | M4 | M5 | M6 | M7 | M8 | M9 | M10 | M11 | M12 | M13 | M14 | M15
TACO-CSR | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
TACO-BCSR | 0.88 | 0.85 | 1.03 | 1.01 | 1.02 | 1.04 | 1.03 | 0.95 | 1.05 | 1.24 | 1.01 | 1.04 | 1.08 | 1.23 | 1.2
SMASH | 1.28 | 1.32 | 1.33 | 1.34 | 1.42 | 1.35 | 1.36 | 1.44 | 1.41 | 1.46 | 1.44 | 1.38 | 1.4 | 1.45 | 1.42
Sparsity sweep for SpMV
SMASH provides speedups regardless
of the sparsity of the matrix
Compression ratio sensitivity analysis
Distribution of non-zero elements
Detailed results for SpMM
Conversion from CSR to SMASH overhead
Software-only approaches
SMASH configuration
  Support for 4 matrices in the BMU
  256 bytes / SRAM buffer
  140 bytes for registers & counters
0.076% area overhead over an Intel Xeon CPU
SMASH incurs negligible area overhead
Recommender Systems
Graph Analytics
Neural Networks
Limitations of Existing Compression Formats
Sparse Matrix Operations are widespread today
1
BITMAP
0
0
0
0
0
0
0
0
0
0
0
0
1
1
Might contain high number of zero bits
MATRIX
NZ
ZEROS
ZEROS
ZEROS
ZEROS
ZEROS
ZEROS
ZEROS
ZEROS
ZEROS
ZEROS
ZEROS
ZEROS
NZ
NZ
ZEROS
0
7: Use Case: SpMV
NZ
NZA
VECTOR
BMU
0
1
0
0
1
0
0
1
0
1
0
0
0
1
0
1
0
0
Matrix Parameters
Bitmap Parameters
COLUMN
INDEX
ROW
INDEX
NZ
NZ
NZ
NZ
NZ
NZ
NZ
NZ
NZ
NZ
NZ
STREAM THROUGH
THE NON-ZERO BLOCKS
INDEX THE VECTOR
USING THE BMU
Many instructions needed to discover
the position of a non-zero element
Scan for full paper
6: Cross-Layer Interface
MATINFO
BMAPINFO
RDBMAP
RDIND
PBMAP
Need for a cross-layer interface that enables software to control the BMU
Communicate the parameters needed to calculate the index
Query the BMU to retrieve the index of the next non-zero element
SMASH ISA
Enables SMASH to flexibly accelerate a diverse range of operations on any sparse matrix
Extremely sparse matrices require compression to
avoid storage and computational overheads