## Slide 1: Spira Exploiting Voxel Data Structural Properties for Efficient Sparse Convolution in Point Cloud Networks
Dionysios Adamopoulos,
Anastasia Poulopoulou, Georgios Goumas, Christina Giannoula
MLSys 2026
Bellevue, USA, May 22nd, 2026

## Slide 2: Executive Summary
Motivation: Sparse Convolution (SpC) is a key operator in point cloud networks widely used in
autonomous driving, robotics, AR/VR…
Spira: The first SpC engine for point cloud networks on GPUs that
intelligently leverages structural properties of voxel data
effectively mitigates pre- and post-processing costs in the SpC mapping step
Opportunities: We identify that SpC operates on voxel data that have inherent structural properties, which existing works do not exploit them
Key Results: Spira improves inference performance over existing state-of-the-art frameworks by 1.68× averaged across six GPU architectures
Problem: SpC execution on GPUs has a mapping step and a feature computation step; prior works incur significant pre- and post-processing overheads in the mapping step of SpC
Spira is open-source:
GitHub

## Slide 3: Outline
Background
Prior Works
Voxel Data Properties
Spira Design
Evaluation

## Slide 4: LiDAR Scanners Collect 3D Point Clouds
LiDAR Scanners
capture
3D Point Clouds
Voxelized Point Cloud
(abbr. voxel data)
Transformed into 3D discrete cubes (voxels)
that are grid-aligned

## Slide 5: Point Cloud Networks Rely on Sparse Convolution (SpC)
Point cloud networks efficiently process voxel data using Sparse Convolution
highly sparse (usually less than 1%)
zero voxel at (x, y, z) location
non-zero voxel at (x, y, z) location
Sparse
Convolution
Batch
Normalization
ReLU
Activation
Batch
Normalization
…
Sparse
Convolution
ReLU
Activation
Voxel data

## Slide 6: SpC Preserves the Sparsity in Output
Q2
Q3
Q5
Q4
Q6
Q1
Q0
Q: Output Non-Zero Coord.
Q2
Q3
P5
Q4
P6
Q1
Q0
P2
P3
P4
P1
P0
P: Input Non-Zero Coord.
W1
W2
W3
W4
W6
W7
W8
W5
W0
W: Weights

## Slide 7: The 2 Steps of SpC
The Mapping Step
The Feature Computation Step
P3
offs(W0)
+
=
1. mapping
2 .feature computation
FP: Features
FQ: Features
x
W0
=
Q2
Q3
Q5
Q4
Q6
Q1
Q0
Q2
Q3
P5
Q4
P6
Q1
Q0
P2
P3
P4
P1
P0
P: Input Non-Zero Coord.
W1
W2
W3
W4
W6
W7
W8
W5
W0
W: Weights
F: Feature
Q4
guides
Q: Output Non-Zero Coord.

## Slide 8: The 2 Steps of SpC
P3
offs(W0)
+
=
1. mapping
2 .feature computation
FP: Features
FQ: Features
x
W0
=
Q4
(generated) Queries
Q4
+
=
offs(W0)
Search Phase
P?
Mappings
Q4
offs(W0)
P3
found!

## Slide 9: The Search Phase of the Mapping Step
(generated) Queries
offs(W0) offs(W1) offs(W2) …
Kernel Map
Q4
+
P?
=
P: Input Non-Zero Coord.
Creates the mappings between the input, weights and output non-zero voxels
searches
offs(W0)
P0
P1
P2
P3
P4
Mappings
Q4
offs(W0)
P3
Q4
…
Q0
Q1
Q2
Q3
invalid entry
(no mapping)
valid entry
(mapping found)
found!
Search Phase

## Slide 10: The 2 Steps of SpC
OR
P3
offs(W0)
1. mapping
Q4
2 .feature computation
FP: Features
FQ: Features
x
W0
(A) Output-Stationary execution dataflow
(B) Weight-Stationary execution dataflow
(generated) Queries
Q4
+
=
offs(W0)
Search Phase
P?
Mappings
Q4
offs(W0)
P3
found!

## Slide 11: Two Dataflows for the Feature Computation Step
offs(W0) offs(W1) offs(W2) …
offs(W0) offs(W1) offs(W2) …
performs better when having
small #invalid entries (dense-friendly)
performs better when having
large #invalid entries (sparse-friendly)
Kernel Map
(row-major)
Kernel Map
(column-major + filtered)
Thread Block 1
Thread Block 2
Thread Block 1
Thread Block 2
consecutive elems in memory
Two different execution dataflows about how to process the kernel map and produce the output features
consecutive elems in memory
invalid entry
valid entry
Either dataflow performs best depending on data and layer characteristics
(A) Output-Stationary execution dataflow
(B) Weight-Stationary execution dataflow

## Slide 12: Outline
Background
Prior Works
Voxel Data Properties
Spira Design
Evaluation

## Slide 13: Prior Works Have a Pre-Process Phase in the Mapping Step
Pre-process Phase
P0
P1
P2
P3
P4
Sorted Input Coord. Array
P: Input Non-Zero Coord.
(pre-processed)
pre-process
…
P4
P3
P0
P1
P2
P: Input Non-Zero Coord.
searches
Prior works introduce pre-processing the input coordinates before the search phase
Queries
Q4
+
P?
=
offs(W0)
Search Phase
Mappings
Q4
offs(W0)
P3
Q4
…
Q0
Q1
Q2
Q3
…
P4
P3
P0
P1
P2
offs(W0) offs(W1) offs(W2) …
Kernel Map
…
Sorted Input Coord. Array

## Slide 14
P3
offs(W0)
1. mapping
Q4
2 .feature computation
FP: Features
FQ: Features
x
W0
Pre-process Phase
(generated) Queries
Q4
+
=
offs(W0)
Search Phase
P?
Mappings
Q4
offs(W0)
P3
found!
Prior Works Incur Large Pre-Processing Costs
OR
(A) Output-Stationary execution dataflow
(B) Weight-Stationary execution dataflow
  e.g., Minuet [Yang et al., EuroSys’24]  pre-processing time is almost equal to search time

## Slide 15: Prior Works Have a Post-Process Phase in the Mapping Step
Prior works need to perform post-processing on the kernel map to support both output- and weight-stationary dataflows
Kernel Map
(row major)
Post-process Phase
Kernel Map
(column major)
offs(W0) offs(W1) offs(W2) …
Kernel Map
(column major + filtered)
transpose
filter
offs(W0) offs(W1) offs(W2) …
offs(W0) offs(W1) offs(W2) …

## Slide 16
OR
(A) Output-Stationary execution dataflow
(B) Weight-Stationary execution dataflow
P3
offs(W0)
1. mapping
Q4
2 .feature computation
FP: Features
FQ: Features
x
W0
Pre-process Phase
(generated) Queries
Q4
+
=
offs(W0)
Search Phase
P?
Mappings
Q4
offs(W0)
P3
found!
Post-process Phase
  Minuet [Yang et al., EuroSys’24]  only weight-stationary dataflow
  TorchSparse++ [Tang et al., MICRO’23]  post-processing costs
  up to ~40% of a layer in the weight-stationary dataflow
Prior Works Incur Large Post-Processing Costs

## Slide 17: Outline
Background
Voxel Data Properties
Spira Design
Evaluation
Prior Works

## Slide 18: Identified Voxel Structural Properties
We identify three properties regarding real-world voxel data:
Voxel data
Integer Property
Bounded Property
Neighboring Property

## Slide 19: Integer Property
Voxel coordinates are integer-valued: a triplet of values represents a discrete location in a 3D grid
Non-zero coordinate at (x, y, z) location
(42,7,12)
integer values

## Slide 20: Bounded Property
Voxel coordinates are spatially constrained due to technological sensor limits
limited capture range of
LiDAR sensors
Non-zero coordinate at (x, y, z) location
(0,0,0) < (42,7,12) < (800,800,100)
bounded range

## Slide 21: Neighboring Property
Neighboring voxel coordinates of the same object surface are likely to exist in small offset displacements
small offset: same object surface
large offset: no same object surface
z
y
x
Existing SpC engines [e.g., TorchSparse++’23, Minuet’24]
do not leverage structural properties of voxel data

## Slide 22: Outline
Background
Spira Design
Evaluation
Prior Works
Voxel Data Properties

## Slide 23: Designing Spira
The first voxel-property-aware SpC engine
Spira incorporates 4 key components:
One-Shot Z-Delta Search Mapping
Packed-Native Mapping Step
Adaptive Hybrid Dataflow Execution
Network-Wide Mapping

## Slide 24: One-Shot Search in the Mapping Step
Spira eliminates pre-processing by directly searching on the sorted input coordinates as given
Pre-process Phase
P: Input Non-Zero Coord.
(pre-processed)
Pre-process
…
P4
P3
P0
P1
P2
P: Input Non-Zero Coord.
searches
Queries
Q4
+
P?
=
offs(W0)
Search Phase
Mappings
Q4
offs(W0)
P3
Q4
…
Q0
Q1
Q2
Q3
…
P4
P3
P0
P1
P2
offs(W0) offs(W1) offs(W2) …
Kernel Map
P0
P1
P2
P3
P4
…
Sorted Input Coord. Array
Existing Works
Spira

## Slide 25: Key Observation on Consecutive Weight Offsets
searches
Queries
Q4
+
P?
=
offs(W0)
Sorted Input Coord. Array
P0
P1
P2
P3
P4
…

## Slide 26: Key Observation on Consecutive Weight Offsets
W1
W2
W3
W4
W6
W7
W8
W5
W0
W: Weights
offs(W0), offs(W1), offs(W2):
identical x, y values +
consecutive z values
e.g., (0,0,-1) (0,0,0) (0,0,1)
K size
offs(W0) = (0,0,-1)
offs(W1) = (0,0,0)
offs(W2) = (0,0,1)
Q4
(50,4,6)
+
Output Coordinate
Consecutive Weight Offsets
Generated Consecutive Queries
Consecutive weight offsets in z-axis produce consecutive queries
identical x, y values +
consecutive z values
(50,4,5) = P?
(50,4,6) = P?
(50,4,7) = P?
K size
K size
Integer Property

## Slide 27: One-Shot Z-Delta Search Mapping
Generated Consecutive Queries
(50,4,5) = P?
(50,4,6) = P?
(50,4,7) = P?
K size
Integer Property
(50,2,3)
(50,3,9)
(50,4,1)
(50,4,5)
(50,4,6)
(50,4,7)
(50,5,3)
P0
P1
P2
P3
P4
P5
P6
K consecutive queries can only map to
up to K consecutive elements in the sorted input coordinates
K size
(50,4,5) = P3
(50,4,5)
. . .
 binary search
Binary
search
(50,4,6)
(50,4,7)
. . .
 linear search
(50,4,6) = P4
(50,4,7) = P5
Linear
search
offs(W0) = (0,0,-1)
offs(W1) = (0,0,0)
offs(W2) = (0,0,1)
Q4
(50,4,6)
+
Output Coordinate
Consecutive Weight Offsets
K size
Sorted Input Coord. Array
P0
P1
P2
P3
P4
…

## Slide 28: Designing Spira
The first voxel-property-aware SpC engine
Spira incorporates the following 4 key components:
No pre-processing costs
High data locality
~K× less binary searches
One-Shot Z-Delta Search Mapping
Packed-Native Mapping Step
Adaptive Hybrid Dataflow Execution
Network-Wide Mapping

## Slide 29: Packed-Native Mapping Step
Key Idea: pack all coordinates into a single integer number (32-bit or 64-bit)
Pack only once at the network start; perform mapping steps as packed-native
three coordinates
32 bits
32 bits
32 bits
Voxel Coordinates require less bits in the x-, y-, z- axis
X
32 bits
one packed coordinates
Y
Z
X|Y|Z
Prior Works
Spira
Integer Property
Bounded Property
memory footprint and computation cost gain

## Slide 30: Designing Spira
The first voxel-property-aware SpC engine
Spira incorporates the following 4 key ideas:
~3× less #comparisons
~3× less #memory accesses
Packed-Native Mapping Step
Adaptive Hybrid Dataflow Execution
Network-Wide Mapping
One-Shot Z-Delta Search Mapping
No pre-processing costs
High data locality
~K× less binary searches

## Slide 31: Adaptive Hybrid Dataflow Execution
offs(W0) offs(W2) offs(W5) offs(W1) offs(W3) offs(W4) offs(W6) …
Kernel Map
#valid entries
#valid entries
Columns associated to smaller offset displacements have larger #valid entries in the Kernel Map
Neighboring Property

## Slide 32: Adaptive Hybrid Dataflow Execution
offs(W0) offs(W2) offs(W5) offs(W1) offs(W3) offs(W4) offs(W6) …
Kernel Map
output-stationary exec.
#valid entries
weight-stationary exec.
#valid entries
Different weight offsets in kernel map can be processed with either output- or weight-stationary dataflow execution
tunable configuration
Neighboring Property

## Slide 33: Dataflow-Aware Kernel Map Post-Processing
Three possible dataflow scenarios:

## Slide 34: Dataflow-Aware Kernel Map Post-Processing
Three possible dataflow scenarios:
3. Hybrid-Dual: directly materialized as column-major
offs(W0) offs(W2) offs(W5) offs(W1) offs(W3) offs(W4) offs(W6) …
output-stationary exec.
weight-stationary exec.
Kernel Map

## Slide 35: Dataflow-Aware Kernel Map Post-Processing
Three possible dataflow scenarios:
3. Hybrid-Dual: directly materialized as column-major
filter only the part processed by weight-stat
transpose only the part processed by output-stat
output-stationary exec.
weight-stationary exec.
Kernel Map
offs(W0) offs(W2) offs(W5) offs(W1) offs(W3) offs(W4) offs(W6) …

## Slide 36: Dataflow-Aware Kernel Map Post-Processing
Three possible dataflow scenarios:
1. Pure Output-Stat: directly materialized as row-major  no post-processing
3. Hybrid-Dual: directly materialized as column-major
offs(W0) offs(W1) offs(W2) offs(W3) offs(W4) offs(W5) offs(W6) …
Kernel Map
output-stationary exec.

## Slide 37: Dataflow-Aware Kernel Map Post-Processing
Three possible dataflow scenarios:
1. Pure Output-Stat: directly materialized as row-major  no post-processing
2. Pure Weight-Stat: directly materialized as column-major 
3. Hybrid-Dual: directly materialized as column-major
offs(W0) offs(W1) offs(W2) offs(W3) offs(W4) offs(W5) offs(W6) …
Kernel Map
weight-stationary exec.

## Slide 38: Dataflow-Aware Kernel Map Post-Processing
Three possible dataflow scenarios:
1. Pure Output-Stat: directly materialized as row-major  no post-processing
2. Pure Weight-Stat: directly materialized as column-major  only filtering
3. Hybrid-Dual: directly materialized as column-major
offs(W0) offs(W1) offs(W2) offs(W3) offs(W4) offs(W5) offs(W6) …
Kernel Map
filter
weight-stationary exec.

## Slide 39: Designing Spira
The first voxel-property-aware SpC engine
Spira incorporates the following 4 key ideas:
Minimal post-processing costs in all dataflows
Adapting execution schema based on data and layer characteristics
Adaptive Hybrid Dataflow Execution
Network-Wide Mapping
One-Shot Z-Delta Search Mapping
Packed-Native Mapping Step
~3× less #comparisons
~3× less #memory accesses
No pre-processing costs
High data locality
~K× less binary searches

## Slide 40: Network-Wide Mapping
Key Observation: Mapping steps have no true dependencies neither with feature computation steps nor between them
Spira executes all mapping steps concurrently at network start and significantly improves GPU SM utilization
Mapping
Batch
Normalization
ReLU
Activation
Batch
Normalization
…
Mapping
ReLU
Activation
Feature Computation
Feature Computation
Mapping
Batch
Normalization
ReLU
Activation
Batch
Normalization
…
Mapping
ReLU
Activation
Feature Computation
Feature Computation
sequential execution of mapping steps
concurrent execution of mapping steps
performance gain
Prior Works
Spira
SpC layer 1
SpC layer 2

## Slide 41: Designing Spira
The first voxel-property-aware SpC engine
Spira incorporates the following 4 key ideas:
Higher execution parallelism
Higher GPU utilization
Network-Wide Mapping
One-Shot Z-Delta Search Mapping
Packed-Native Mapping Step
Adaptive Hybrid Dataflow Execution
Minimal post-processing costs in all dataflows
Adapting execution schema based on data and layer characteristics
~3× less #comparisons
~3× less #memory accesses
No pre-processing costs
High data locality
~K× less binary searches

## Slide 42: Outline
Background
Evaluation
Prior Works
Voxel Data Properties
Spira Design

## Slide 43: Evaluation Methodology
3x Point Cloud Networks: ResNet, Large ResNet, UNet
3x Datasets: Waymo, SemanticKITTI, ScanNet
6x GPUs:
  A100, H100: datacenter
  Quadro RTX 5000: workstation
  GTX 1060, RTX 3090: consumer
  Jetson Orin AGX: edge GPU platform
Comparison points:
  TorchSparse++ [MICRO’23] - supports both output- and weight-stationary dataflow
  Minuet [EuroSys’24] – supports only weight-stationary dataflow

## Slide 44: Inference Performance across Multiple GPUs
Chart: Speedup
| A100 | H100 | Quadro | 1060 | 3090 | Orin
Minuet | 1 | 1 | 1 | 1 | 1 | 1
TorchSparse++ | 1.3 | 1.15 | 1.13 | 0.97 | 1.05 | 0.88
Spira | 2.05 | 1.84 | 1.77 | 1.45 | 1.7 | 1.65
datacenter
workstation
consumer
  edge GPU platform
Spira significantly outperforms prior SpC engines
by 1.68× averaged across six GPUs
Averaged inference results across 3 networks and 3 datasets

## Slide 45: Breakdown of Spira’s Key Ideas
Chart: Breakdown in UNet
| Spira + ZDelta Search + Packing + Hybrid Dual Dataflow + Network-Wide Mapping | Spira + ZDelta Search + Packing + Hybrid Dual Dataflow | Spira + ZDelta Search + Packing | Spira + ZDelta Search | Minuet | TorchSparse++
 | 1.35 | 1.29 | 1.21 | 1.18 | 1.04 | 1
Spira (Z-Delta Search) + Packing + Hybrid Dual Dataflow + Network-wide Mapping
Speedup
Spira (Z-Delta Search) + Packing + Hybrid Dual Dataflow

## Slide 46: More in the Paper
Detailed inference analysis for various datasets and networks
Layer-wise analysis
Hybrid dataflow sensitivity analysis
Mapping step analysis
Effect of network-wide mapping
Input density ablation study
Scalability study
Memory footprint study
https://arxiv.org/abs/2511.20834

## Slide 47: Spira is Open Source
https://github.com/SPIN-Research-Group/Spira
Spira

## Slide 48: Conclusion
GitHub
Paper
Key Results: improves inference performance by on average 1.68× over existing state-of-the-art SpC engines across six GPU architectures, spanning from datacenter to edge GPU devices
Spira is the first SpC engine that leverages structural properties of voxel data and significantly improves performance of point cloud networks on GPUs
Key Ideas & Benefits:
completely eliminates pre-processing costs in the mapping step
enables high data locality and low computational cost in the search phase of the mapping step via an intelligent search algorithm
proposes a packing format that reduces memory accesses and computation cost on voxel coordinate processing
supports a tunable adaptive dataflow schema with low post-processing costs
executes all mapping steps concurrently to improve GPU utilization

## Slide 49: Spira Exploiting Voxel Data Structural Properties for Efficient Sparse Convolution in Point Cloud Networks
Dionysios Adamopoulos,
Anastasia Poulopoulou, Georgios Goumas, Christina Giannoula
MLSys 2026
Bellevue, USA, May 22nd, 2026