## Slide 1: Accelerating Irregular Applications via Efficient Synchronization and Data Access Techniques
Christina Giannoula PhD Thesis Oral
Committee Georgios Goumas (NTUA)
Nectarios Koziris (NTUA)
Onur Mutlu (ETH Zürich)
Dionisios Pnevmatikatos (NTUA)
Stefanos Kaxiras (Uppsala University)
Dimitris Gizopoulos (University of Athens)
Vasileios Papaefstathiou (University of Crete)

## Slide 2
Irregular Applications
Neural Networks
Bioinformatics
Databases
Medical Imaging
Economic Modeling
Graph Analytics
How can we accelerate the irregular applications?

## Slide 3
Characteristic 1: Inherent Imbalance
The objects involved are not of equal size
Sparse Matrix
Power-Law Graph
Zipfian Query Distribution

## Slide 4
Characteristic 2: Random Memory Accesses
Not sequential
Not strided
Input-driven
Diagonal Matrix
Highly Sparse Matrix
Highly Skewed Matrix

## Slide 5
Characteristic 3: Low Operational Intensity
High bottleneck by the memory subsystem
Operational Intensity
Performance
SpMV
Peak CPU Performance
Peak Memory Bandwidth

## Slide 6
Challenge 1: Excessive Synchronization
Inherent Imbalance
Random Memory Accesses
Diagonal
Matrix
Highly
Skewed
Matrix
Coarse-Grained Approach
Thread 1
Thread 2
Thread 3
Thread 1
Thread 2
Thread 3
SpMV
Fine-Grained Approach
Thread 1
Thread 2
Thread 3
Thread 1
Thread 2
Thread 3

## Slide 7
Challenge 1: Excessive Synchronization
Inherent Imbalance
Random Memory Accesses
A large amount of processors’ cycles
is spent on synchronization

## Slide 8
Challenge 2: High Memory Intensity
Random Memory Accesses
Low Operational Intensity
The SpMV Execution
input vector
accesses
input vector
accesses
input vector
accesses
*
Row 1
Sparse Matrix
*
Row 2
Sparse Matrix
*
Row 3
Sparse Matrix

## Slide 9
Challenge 2: High Memory Intensity
Random Memory Accesses
Low Operational Intensity
A large amount of processors’ cycles
is spent on data accesses

## Slide 10
Challenge 2: High Memory Intensity
Random Memory Accesses
Low Operational Intensity
Processors
Cache
Memory
Data
Uniform Systems
Network
Processors
Cache
Memory
Data
Network
Processors
Cache
Memory
Data
Network
Non-Uniform / Heterogeneous Systems
Network
The Era of Heterogeneity

## Slide 11
Our Approach
Synchronization of Threads
+
Management of Data
The two major priorities
in the execution
of irregular applications

## Slide 12
Our Approach
Efficient Synchronization
+
Efficient Data Management
The two major priorities
in the execution
of irregular applications
High load balance
Low-cost inter-thread communication
High levels of parallelism
Low-cost data accesses
High memory bandwidth

## Slide 13
Thesis Statement
Low-overhead synchronization approaches
in cooperation with
well-crafted data access techniques
can significantly improve
performance and energy efficiency
of emerging irregular applications.

## Slide 14
Thesis Goal
Processors
Cache
Processors
Cache
Main Memory
Main Memory
CPU System
(processor-centric)
Host CPU
Cache
Processing-In-Memory (PIM) System
(memory-centic)
PIM-Enabled Memory
Memory Arrays
Processor
Memory Arrays
Processor
PIM-Enabled Memory
Memory Arrays
Processor
Memory Arrays
Processor
Irregular Applications: important yet difficult
Bioinformatics
Databases
Graph Analytics

## Slide 15
Core Contributions
Processors
Cache
Processors
Cache
Main Memory
Main Memory
CPU System
Host CPU
Cache
PIM System
PIM-Enabled Memory
Memory Arrays
Processor
Memory Arrays
Processor
PIM-Enabled Memory
Memory Arrays
Processor
Memory Arrays
Processor
ColorTM (ISC’18, SRC PACT’18) High-Performance Graph Coloring for CPU Systems
Graph Processing
1
SynCron (HPCA’21) A Lightweight Synchronization Mechanism for PIM Systems
Irregular
Workloads
3
SmartPQ (CF’19) An Adaptive Priority Queue for NUMA CPU Systems
Pointer-Chasing
2
SparseP (Sigmetrics’22) A Library of Efficient Sparse Matrix Vector Multiplication Kernels for Real PIM Systems
Sparse Linear Algebra
4

## Slide 16
Core Contributions
Processors
Cache
Processors
Cache
Main Memory
Main Memory
CPU System
Host CPU
Cache
PIM System
PIM-Enabled Memory
Memory Arrays
Processor
Memory Arrays
Processor
PIM-Enabled Memory
Memory Arrays
Processor
Memory Arrays
Processor
ColorTM (ISC’18, SRC PACT’18) High-Performance Graph Coloring for CPU Systems
Graph Processing
1
Trade-off between using synchronization
with lower data access costs

## Slide 17
Graph Coloring
Chromatic Scheduling
The Problem
Applications: PageRank, Community Detection, Resource Allocation …
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Time
How can we accelerate
the graph coloring kernel?

## Slide 18
Prior Parallel Algorithms
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Processor
Main Memory
Processor
Parallel Graph Coloring – No Synchronization
1

## Slide 19
Prior Parallel Algorithms
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Processor
Main Memory
Processor
Parallel Graph Coloring – No Synchronization
1
Detect Coloring Conflicts
2

## Slide 20
Prior Parallel Algorithms
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Processor
Main Memory
Processor
Parallel Graph Coloring – No Synchronization
1
Detect Coloring Conflicts
2
Resolve Coloring Conflicts Sequentially
3
Sequential Solving (SeqSolve [Gebr.+’00])

## Slide 21
Prior Parallel Algorithms
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Processor
Main Memory
Processor
Parallel Graph Coloring – No Synchronization
1
Detect Coloring Conflicts
2
Repeat Steps 1 + 2 Multithreaded
3
Iterative Solving (IterSlv [Boman.+’05], IterSlvR [Rokos.+’15])

## Slide 22
Prior Parallel Algorithms
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Lazy Iterative Coloring (e.g., SeqSlv, IterSlv, IterSlvR)
Main Memory
Time
Data Access Costs
Conflict
Arising
Conflict
Detection
Conflict
Resolution
Cache
Main Memory

## Slide 23
Prior Parallel Algorithms
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Lazy Iterative Coloring (e.g., SeqSlv, IterSlv, IterSlvR)
At least 2 iterations on the whole graph
Lazy coloring conflict detection + resolution
 | SeqSlv | IterSlv | IterSlvR
Parallelism |  |  | 
Synchronization |  |  | 
Data Accesses |  |  | 

## Slide 24
ColorTM [ISC’18, SRC PACT’18]
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Eager Iterative Coloring
Eager coloring conflict detection + resolution
Speculative computation + synchronization
 | SeqSlv | IterSlv | IterSlvR | ColorTM
Parallelism |  |  |  | 
Synchronization |  |  |  | 
Data Accesses |  |  |  | 

## Slide 25
ColorTM: Key Idea 1
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Eager Conflict Detection + Resolution
Iterate on each vertex until a valid coloring is found
Processor
Main Memory
Cache
Processor
Cache
    Low Data Access Costs
    Low Latency

## Slide 26
ColorTM: Key Idea 2
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Speculative Synchronization + Computation
Employ hardware transactional memory
Perform most computations speculatively – outside the critical section
find_speculative_color();
1
begin_HTM();
2
validate_color();
3
end_HTM();
4
Iterate on
each vertex
    Low Synchronization Costs
    High Amount of Parallelism

## Slide 27
Performance Analysis
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Chart: Real-World Graphs
| qun | geo | fln | bum | ser | del | rgg | kmr | cag | usa | dlf | aud | vas | stk | uk | soc | arb | fch | GM
SeqSlv | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
IterSlv | 4.6561 | 4.9501 | 4.8864 | 4.704 | 4.8982 | 0.7163 | 0.9697 | 0.69652 | 5.5186 | 0.73906 | 5.3511 | 5.2267 | 6.1172 | 5.9518 | 2.0788 | 2.5937 | 3.5673 | 3.4685 | 2.9821
IterSolvR | 0.33526 | 0.41549 | 0.33583 | 0.37495 | 0.45684 | 0.059144 | 0.11244 | 0.0659 | 0.66562 | 0.05723 | 0.59956 | 0.48027 | 0.81568 | 0.79944 | 0.25059 | 0.33607 | 0.51012 | 0.51331 | 0.30602
ColorTM | 14.5816 | 14.5737 | 14.3609 | 15.097 | 22.4875 | 1.462 | 7.882 | 1.2948 | 15.7492 | 1.5751 | 13.6155 | 21.5682 | 13.2558 | 14.0603 | 14.0972 | 3.8298 | 6.8144 | 6.4449 | 8.4646
2.84x

## Slide 28
Balanced ColorTM
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Balanced Chromatic Scheduling
Imbalanced Chromatic Scheduling
=
Low Resource Utilization
High Resource Utilization
Time
Slot1
Slot2
Slot3
Slot4
Slot5
Time
Slot1
Slot2
Slot3
Slot4
Slot5
1.91x faster than prior works using 56 threads
Community Detection: 1.12x faster over the imbalanced variant using 56 threads

## Slide 29
Core Contributions
Processors
Cache
Processors
Cache
Main Memory
Main Memory
CPU System
Host CPU
Cache
PIM System
PIM-Enabled Memory
Memory Arrays
Processor
Memory Arrays
Processor
PIM-Enabled Memory
Memory Arrays
Processor
Memory Arrays
Processor
SmartPQ (CF’19) An Adaptive Priority Queue for NUMA CPU Systems
Pointer-Chasing
2
High contention  low data access costs
Low contention  lightweight synchronization

## Slide 30
Motivation
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Priority Queues (PQs) are widely used in graph processing kernels, discrete event simulations …
Key Observations:
  PQs exhibit medium contention
insert()
deleteMin()
Low Contetion
High Contetion

## Slide 31
Motivation
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Priority Queues (PQs) are widely used in graph processing kernels, discrete event simulations …
Key Observations:
  PQs exhibit medium contention
  Neither a prior NUMA-aware nor NUMA-oblivious PQ always performs best in a NUMA CPU architecture
Chart: 1024 Elements / 2048 Key Range / 64 Threads
| 70% - 30% | 50% - 50% | 30% - 70%
NUMA-Oblivious | 21.5 | 1.3 | 0.8
NUMA-Aware | 3 | 2.5 | 4.5
21.5x
NUMA-Oblivious
NUMA-Aware
NUMA-Aware
Can we design an ‘intelligent’ PQ to always perform best?

## Slide 32
Key Contributions
ColorTM
SmartPQ
SynCron
SparseP
Future Work
A black-box approach to provide high-performance NUMA-aware Concurrent Data Structures (CDSs)
An adaptive PQ to perform best under various contention workloads
Framework
NUMA-Oblivious
CDSs
NUMA-Aware CDSs
Nuddle:
NUMA-Aware PQ
NUMA-Oblivious
PQ
SmartPQ:

## Slide 33
1. NUMA Node Delegation (Nuddle)
ColorTM
SmartPQ
SynCron
SparseP
Future Work
A generic framework to design NUMA-aware CDSs
Processor
(server thread)
Cache
Main Memory
Processor
(server thread)
Processor
(server thread)
Processor
(client
thread)
Cache
Processor
(client
thread)
Processor
(client
thread)
Main Memory
Processor
(client thread)
Cache
Processor
(client thread)
Processor
(client thread)
Main Memory
Data Structure
Data Structure
NUMA Node 0
NUMA Node 2
NUMA Node 1

## Slide 34
1. NUMA Node Delegation (Nuddle)
ColorTM
SmartPQ
SynCron
SparseP
Future Work
A generic framework to design NUMA-aware CDSs
Processor
(server thread)
Cache
Main Memory
Processor
(server thread)
Processor
(server thread)
Processor
(client
thread)
Cache
Processor
(client
thread)
Processor
(client
thread)
Main Memory
Processor
(client thread)
Cache
Processor
(client thread)
Processor
(client thread)
Main Memory
Data Structure
Data Structure
NUMA Node 0
NUMA Node 2
NUMA Node 1
response msg (up 15 clients) [Roghanchi+ SOSP’17]: 1 cache line
request msg (1 client) [Roghanchi+ SOSP’17]: 1 cache line

## Slide 35
1. NUMA Node Delegation (Nuddle)
ColorTM
SmartPQ
SynCron
SparseP
Future Work
A generic framework to design NUMA-aware CDSs
Processor
(server thread)
Cache
Main Memory
Processor
(server thread)
Processor
(server thread)
Processor
(client
thread)
Cache
Processor
(client
thread)
Processor
(client
thread)
Main Memory
Processor
(client thread)
Cache
Processor
(client thread)
Processor
(client thread)
Main Memory
Data Structure
Data Structure
NUMA Node 0
NUMA Node 2
NUMA Node 1
Any NUMA-oblivious  NUMA-aware CDS
Minimizes the memory traffic
Low-overhead communication protocol
Needs synchronization
Parallelization is limited to the number of server threads

## Slide 36
2. SmartPQ
ColorTM
SmartPQ
SynCron
SparseP
Future Work
An adaptive PQ that switches between two algorithmic modes whenever it is needed
NUMA-Oblivious
PQ
NUMA-Aware PQ

## Slide 37
2. SmartPQ
ColorTM
SmartPQ
SynCron
SparseP
Future Work
An adaptive PQ that switches between two algorithmic modes whenever it is needed
Key Challenges:
How to switch between the two modes with low synchronization overheads?
NUMA-Oblivious
PQ
NUMA-Aware PQ
Low Cost?

## Slide 38
2. SmartPQ
ColorTM
SmartPQ
SynCron
SparseP
Future Work
An adaptive PQ that switches between two algorithmic modes whenever it is needed
Key Challenges:
How to switch between the two modes with low synchronization overheads?
NUMA-Oblivious
PQ
Nuddle
Low Cost?
Nuddle
=
NUMA-Oblivious PQ

## Slide 39
2. SmartPQ
ColorTM
SmartPQ
SynCron
SparseP
Future Work
An adaptive PQ that switches between two algorithmic modes whenever it is needed
Key Challenges:
How to switch between the two modes with low synchronization overheads?
When to switch from the one to the other mode?
NUMA-Oblivious
PQ
Nuddle
Low Cost?
Nuddle
NUMA-Oblivious PQ
When?
ML
Decission Tree Classifier
NUMA-Aware, NUMA-Oblivious, Neutral

## Slide 40
2. SmartPQ
ColorTM
SmartPQ
SynCron
SparseP
Future Work
An adaptive PQ that switches between two algorithmic modes whenever it is needed
Key Challenges:
How to switch between the two modes with low synchronization overheads?
When to switch from the one to the other mode?
NUMA-Oblivious
PQ
Nuddle
Low Cost?
Nuddle
NUMA-Oblivious PQ
When?
ML
Decission Tree Classifier
NUMA-Aware, NUMA-Oblivious, Neutral
2-4 ms traversal time with 180 nodes
and a very low tree depth of 8
87.9% accuracy in a test set
of 10K different contention workloads

## Slide 41
Throughput Evaluation
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Chart: 40% - 60% insert() - deleteMin() Ratio
| 2 | 4 | 8 | 15 | 22 | 29 | 36 | 43 | 50 | 57 | 106 | 155
alistarh_fraser | 4.0863 | 5.296 | 5.492 | 1.595 | 1.227 | 1.0187 | 1.1073 | 0.84967 | 0.94567 | 1.0193 | 0.91367 | 0.921
alistarh_herlihy | 4.0217 | 5.085 | 5.2583 | 1.729 | 1.1237 | 0.894 | 1.0257 | 0.837 | 0.85333 | 0.83533 | 0.72433 | 0.83533
lotan_shavit | 4.255 | 5.4263 | 5.575 | 1.2803 | 0.888 | 0.75167 | 0.809 | 0.86867 | 0.917 | 0.97233 | 1.0067 | 1.0457
ffwd | 1.9577 | 2.3657 | 2.609 | 2.6223 | 2.6047 | 2.6397 | 2.688 | 2.7337 | 2.7773 | 2.794 | 2.6903 | 1.6127
Nuddle | 4.049 | 5.1503 | 5.329 | 5.1843 | 5.3873 | 5.302 | 5.033 | 5.0857 | 5.206 | 5.1013 | 5.4097 | 5.0963
Chart: 80% - 20% insert() - deleteMin() Ratio
| 2 | 4 | 8 | 15 | 22 | 29 | 36 | 43 | 50 | 57 | 106 | 155
alistarh_fraser | 3.813 | 6.9607 | 12.676 | 10.6677 | 12.9733 | 12.0987 | 17.4997 | 19.3737 | 20.085 | 20.8183 | 19.6147 | 18.1483
alistarh_herlihy | 4.1183 | 7.5283 | 13.793 | 10.6117 | 11.1483 | 13.5943 | 18.6777 | 19.6577 | 22.6223 | 21.7877 | 27.357 | 28.7657
lotan_shavit | 4.2433 | 7.4787 | 11.6863 | 4.2193 | 2.917 | 2.631 | 2.832 | 2.9947 | 3.141 | 3.3133 | 3.383 | 3.4477
ffwd | 1.048 | 1.201 | 1.3197 | 1.302 | 1.2953 | 1.2993 | 1.336 | 1.3317 | 1.3497 | 1.351 | 1.321 | 0.67533
Nuddle | 4.128 | 7.4367 | 13.5347 | 14.1823 | 14.6857 | 15.184 | 14.3807 | 14.827 | 14.4703 | 15.4823 | 14.822 | 14.2953
NUMA-Oblivious
NUMA-Aware
Nuddle
alistarh_herlihy [SIROCCO‘07 + PpopP’15]

## Slide 42
Throughput with Varying Contention
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Chart: Execution Time (s)

## Slide 43
Throughput with Varying Contention
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Chart: Execution Time (s)
1.87x
1.38x

## Slide 44
Core Contributions
Processors
Cache
Processors
Cache
Main Memory
Main Memory
CPU System
Host CPU
Cache
PIM System
PIM-Enabled Memory
Memory Arrays
Processor
Memory Arrays
Processor
PIM-Enabled Memory
Memory Arrays
Processor
Memory Arrays
Processor
SynCron (HPCA’21) A Lightweight Synchronization Mechanism for PIM Systems
Irregular
Workloads
3
Enabling very low synchronization costs

## Slide 45
Processing-In-Memory (PIM) Architecture
Synchronization challenges in PIM systems:
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Main Memory
PIM Core
PIM Core
PIM Core
PIM Unit
Programmable Core / Accelerator
Private Cache
PIM System
(1) Lack of hardware cache coherence support
(2) Lack of a shared level of cache memory
(3) Expensive communication across PIM units

## Slide 46
PIM Synchronization Solution Space
ColorTM
SmartPQ
SynCron
SparseP
Future Work
(1) Shared Memory
(2) Message-passing

## Slide 47
PIM Synchronization Solution Space
SynCron’s Key Techniques:
Hardware support for synchronization acceleration
Direct buffering of synchronization variables
Hierarchical message-passing communication
Integrated hardware-only overflow management
ColorTM
SmartPQ
SynCron
SparseP
Future Work
(1) Shared Memory
(2) Message-passing
PIMs:
SynCron [HPCA’21]

## Slide 48
1. Hardware Synchronization Support
ColorTM
SmartPQ
SynCron
SparseP
Future Work
PIM Unit 0
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 0
PIM Unit 1
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 1
`````
ISA
Local
lock acquire
  No Complex Cache Coherence Protocols
  No Expensive Atomic Operations
  Low Hardware Cost

## Slide 49
2. Direct Buffering of Variables
ColorTM
SmartPQ
SynCron
SparseP
Future Work
PIM Unit 0
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 0
PIM Unit 1
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 1
Indexing Counters
Synchronization
Processing Unit
Synchronization
Table
Address
…
--
…
--
…
--
…
--
…

## Slide 50
2. Direct Buffering of Variables
ColorTM
SmartPQ
SynCron
SparseP
Future Work
PIM Unit 0
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 0
PIM Unit 1
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 1
Indexing Counters
Synchronization
Processing Unit
Synchronization
Table
Local
lock acquire
Address
…
0x33A9
…
--
…
--
…
--
…

## Slide 51
2. Direct Buffering of Variables
ColorTM
SmartPQ
SynCron
SparseP
Future Work
PIM Unit 0
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 0
PIM Unit 1
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 1
Indexing Counters
Synchronization
Processing Unit
Synchronization
Table
Address
…
0x33A9
…
--
…
--
…
--
…
  No Costly Memory Accesses
  Low Latency

## Slide 52
3. Hierarchical Communication
ColorTM
SmartPQ
SynCron
SparseP
Future Work
PIM Unit 0
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 0
PIM Unit 1
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 1
PIM Unit 2
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 2
PIM Unit 3
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 3

## Slide 53
3. Hierarchical Communication
ColorTM
SmartPQ
SynCron
SparseP
Future Work
PIM Unit 0
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 0
PIM Unit 1
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 1
PIM Unit 2
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 2
PIM Unit 3
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 3
Master
Local
lock acquire
syncronVar

## Slide 54
3. Hierarchical Communication
ColorTM
SmartPQ
SynCron
SparseP
Future Work
PIM Unit 0
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 0
PIM Unit 1
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 1
PIM Unit 2
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 2
PIM Unit 3
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 3
Master
Global
lock acquire
syncronVar
  Minimize Expensive Network Traffic

## Slide 55
4. Integrated Overflow Management
ColorTM
SmartPQ
SynCron
SparseP
Future Work
PIM Unit 0
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 0
PIM Unit 1
Main Memory
PIM Core 0
PIM Core 1
Synchronization
Engine 1
Master
syncronVar
Synchronization
Processing Unit
Synchronization
Table
Indexing Counters
Address
…
0x33A9
…
0x2241
…
0x438C
…
0x6B4A
…
Fully Occupied
  Low Performance Degradation
  High Programming Ease

## Slide 56
Throughput of Pointer Chasing
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Chart: 
| 15 | 30 | 45 | 60
Central | 4.72 | 6 | 6.9 | 7.92
Hier | 4.85 | 7.2 | 8.3 | 9.32
SynCron | 4.97 | 7.32 | 8.62 | 9.97
Ideal | 6.66 | 9.82 | 11.55 | 13.8
Operations / μs
Stack – 100K
Number of PIM Cores
Operations / μs
Chart: 
| 15 | 30 | 45 | 60
Hier | 6.08 | 11.72 | 17.02 | 20.55
Central | 6.21 | 9.47 | 11.63 | 12.85
SynCron | 6.57 | 12.67 | 18.38 | 22.88
Ideal | 8.22 | 15.86 | 22.99 | 28.27
Number of PIM Cores
Hash Table – 1K
Chart: 
| 15 | 30 | 45 | 60
Hier | 3.3 | 5.1 | 6.26 | 8.13
Central | 3.3 | 3.63 | 4.38 | 5.73
SynCron | 4.08 | 6 | 7.49 | 9.65
Ideal | 5.53 | 7.97 | 9.66 | 12.57
Linked List – 20K
Number of PIM Cores
Operations / ms
High Contention
Small #Variables
Medium Contention
Medium #Variables
Low Contention
High #Variables

## Slide 57
Throughput of Pointer Chasing
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Chart: 
| 15 | 30 | 45 | 60
Central | 4.72 | 6 | 6.9 | 7.92
Hier | 4.85 | 7.2 | 8.3 | 9.32
SynCron | 4.97 | 7.32 | 8.62 | 9.97
Ideal | 6.66 | 9.82 | 11.55 | 13.8
Operations / μs
Stack – 100K
Number of PIM Cores
Operations / μs
Chart: 
| 15 | 30 | 45 | 60
Hier | 6.08 | 11.72 | 17.02 | 20.55
Central | 6.21 | 9.47 | 11.63 | 12.85
SynCron | 6.57 | 12.67 | 18.38 | 22.88
Ideal | 8.22 | 15.86 | 22.99 | 28.27
Number of PIM Cores
Hash Table – 1K
Chart: 
| 15 | 30 | 45 | 60
Hier | 3.3 | 5.1 | 6.26 | 8.13
Central | 3.3 | 3.63 | 4.38 | 5.73
SynCron | 4.08 | 6 | 7.49 | 9.65
Ideal | 5.53 | 7.97 | 9.66 | 12.57
Linked List – 20K
Number of PIM Cores
Operations / ms
High Contention
Small #Variables
Medium Contention
Medium #Variables
Low Contention
High #Variables
1.18x
1.26x
1.59x
1.78x
1.19x
1.68x
1.18x
1.26x
1.59x
1.78x
1.19x
1.68x

## Slide 58
Performance in Data Analytics
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Chart: Speedup
| bfs.sl | cc.sx | sssp.co | pr.wk | tf.sl | tc.sx | ts.air | ts.pow | AVG
Central | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Hier | 1.09 | 1.11 | 1.07 | 1.25 | 1.09 | 1.12 | 1.67 | 1.63 | 1.19
SynCron | 1.38 | 1.37 | 1.21 | 1.5 | 1.38 | 1.41 | 2.16 | 2.29 | 1.48
Ideal | 1.46 | 1.43 | 1.42 | 1.61 | 1.48 | 1.49 | 2.88 | 2.63 | 1.58
-9.5%
1.23x

## Slide 59
System Energy in Data Analytics
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Chart: Energy Breakdown
| Central | Hier | SynCron | Ideal | Central | Hier | SynCron | Ideal | Central | Hier | SynCron | Ideal | Central | Hier | SynCron | Ideal | Central | Hier | SynCron | Ideal | Central | Hier | SynCron | Ideal | Central | Hier | SynCron | Ideal | Central | Hier | SynCron | Ideal | Central | Hier | SynCron | Ideal | bfs.sl | cc.sx | sssp.co | pr.wk | tf.sl | tc.sx | ts.air | ts.pow | AVG
Cache | 0.0473 | 0.0472 | 0.0427 | 0.0431 | 0.1523 | 0.1522 | 0.1411 | 0.1412 | 0.0514 | 0.0513 | 0.0504 | 0.0502 | 0.0432 | 0.0428 | 0.0425 | 0.0426 | 0.0562 | 0.0561 | 0.0546 | 0.0545 | 0.0465 | 0.0462 | 0.0449 | 0.0447 | 0.0174 | 0.0175 | 0.018 | 0.0176 | 0.0158 | 0.0158 | 0.0159 | 0.0158 | 0.060261 | 0.059413 | 0.055142 | 0.043096
Network | 0.1324 | 0.0645 | 0.0477 | 0.0335 | 0.1543 | 0.0831 | 0.0697 | 0.0571 | 0.1645 | 0.0714 | 0.0543 | 0.0382 | 0.1769 | 0.0874 | 0.0732 | 0.0596 | 0.1658 | 0.0867 | 0.0684 | 0.0524 | 0.17 | 0.086 | 0.071 | 0.0558 | 0.2784 | 0.0818 | 0.0604 | 0.0317 | 0.2441 | 0.0671 | 0.0474 | 0.0207 | 0.17129 | 0.079855 | 0.065467 | 0.038031
Memory | 0.8203 | 0.8112 | 0.3902 | 0.3891 | 0.6935 | 0.678 | 0.3501 | 0.3408 | 0.7841 | 0.7654 | 0.3409 | 0.3251 | 0.78 | 0.7275 | 0.3734 | 0.3628 | 0.778 | 0.7625 | 0.3055 | 0.298 | 0.7835 | 0.7349 | 0.3597 | 0.3371 | 0.7042 | 0.6917 | 0.1568 | 0.1565 | 0.7401 | 0.7247 | 0.2334 | 0.232 | 0.76845 | 0.74027 | 0.33961 | 0.32773
1.94x
-6.2%

## Slide 60
Core Contributions
Processors
Cache
Processors
Cache
Main Memory
Main Memory
CPU System
Host CPU
Cache
PIM System
PIM-Enabled Memory
Memory Arrays
Processor
Memory Arrays
Processor
PIM-Enabled Memory
Memory Arrays
Processor
Memory Arrays
Processor
SparseP (Sigmetrics’22) A Library of Efficient Sparse Matrix Vector Multiplication Kernels for Real PIM Systems
Sparse Linear Algebra
4
Across multiple PIM cores  low data transfer costs
Across multiple threads  lightweight synchronization

## Slide 61
Motivation
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Sparse Matrix Vector Multiplication (SpMV):
  Widely used in machine learning, graph analytics, scientific computing…
  A highly bandwidth-bound kernel
Operational Intensity
Performance
Peak Compute Performance
Peak Memory Bandwidth
SpMV
Roofline Model

## Slide 62
Motivation
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Sparse Matrix Vector Multiplication (SpMV):
  Widely used in machine learning, graph analytics, scientific computing…
  A highly bandwidth-bound kernel
Real Near-Bank Processing-In-Memory (PIM) Systems:
  High levels of parallelism
  Large aggregate memory bandwidth
Host CPU
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Bus
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
Main Memory
DRAM Bank
DRAM Bank
DRAM Bank
DRAM Bank
Bus

## Slide 63
Key Contributions
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Design efficient SpMV kernels for current and future PIM systems
  SparseP = 25 SpMV kernels
Provide a comprehensive analysis of SpMV on the first commercially-available real PIM system
  26 sparse matrices
  Comparisons to state-of-the-art CPU and GPU systems
  Recommendations for software, system and hardware designers
SparseP: https://github.com/CMU-SAFARI/SparseP
SparseP is Open-Source
Full Paper: https://arxiv.org/pdf/2201.05072.pdf
Recommendations for Architects and Programmers

## Slide 64
SpMV Execution on a PIM System
ColorTM
SmartPQ
SynCron
SparseP
Future Work
bus
bus
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host CPU
+
Load the
input vector
Execute the kernel
Retrieve the
partial results
Merge the
partial results
1
2
3
4
Main Memory
DRAM Bank
DRAM Bank

## Slide 65
Compute-Aware vs Data-Aware SpMV
ColorTM
SmartPQ
SynCron
SparseP
Future Work
SparseP supports two types of data partitioning techniques:
1D Partitioning
(compute-aware)
=
1x output vector
*
4x input vector
Core 1
Core 2
Core 3
Core 4
perform the complete
SpMV computation
only on PIM cores
2D Partitioning
(data-aware)
2x output vector
=
2x input vector
*
Core 1
Core 2
Core 3
Core 4
trade-off
computation vs
data transfer costs

## Slide 66
Compute-Aware vs Data-Aware SpMV
ColorTM
SmartPQ
SynCron
SparseP
Future Work
From 64 up to 2528 PIM Cores, 32-bit float
Chart: Speedup
| hgc | mc2 | pfm | rtn | rjt | ash | del | tdk | mem | amz | fth | wbg | ldr | psb | bns | wbs | in | pks | cmb | sxw | skt | ask | GM (1) | GM (2)
1D (compute-aware) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
2D (data-aware) | 1.1069 | 1.0513 | 1.369 | 1.0535 | 1.3571 | 1.4257 | 1.6339 | 1.4236 | 1.4165 | 1.2136 | 1.2889 | 1.368 | 1.2745 | 1.3837 | 1.3542 | 0.81272 | 0.35968 | 0.95352 | 0.87023 | 0.49709 | 0.87267 | 0.74493 | 1.3057 | 0.69507
1.45x
1.31x
regular
scale-free

## Slide 67
Compute-Aware vs Data-Aware SpMV
ColorTM
SmartPQ
SynCron
SparseP
Future Work
From 64 up to 2528 PIM Cores, 32-bit float
Chart: Speedup
| hgc | mc2 | pfm | rtn | rjt | ash | del | tdk | mem | amz | fth | wbg | ldr | psb | bns | wbs | in | pks | cmb | sxw | skt | ask | GM (1) | GM (2)
1D (compute-aware) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
2D (data-aware) | 1.1069 | 1.0513 | 1.369 | 1.0535 | 1.3571 | 1.4257 | 1.6339 | 1.4236 | 1.4165 | 1.2136 | 1.2889 | 1.368 | 1.2745 | 1.3837 | 1.3542 | 0.81272 | 0.35968 | 0.95352 | 0.87023 | 0.49709 | 0.87267 | 0.74493 | 1.3057 | 0.69507
regular
scale-free
>1100 Idle Cores
>2200 Idle Cores
Best-performing SpMV execution:
trades off computation
with lower data transfer costs

## Slide 68
Compute-Aware vs Data-Aware SpMV
ColorTM
SmartPQ
SynCron
SparseP
Future Work
From 64 up to 2528 PIM Cores, 32-bit float
Chart: Speedup
| hgc | mc2 | pfm | rtn | rjt | ash | del | tdk | mem | amz | fth | wbg | ldr | psb | bns | wbs | in | pks | cmb | sxw | skt | ask | GM (1) | GM (2)
1D (compute-aware) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
2D (data-aware) | 1.1069 | 1.0513 | 1.369 | 1.0535 | 1.3571 | 1.4257 | 1.6339 | 1.4236 | 1.4165 | 1.2136 | 1.2889 | 1.368 | 1.2745 | 1.3837 | 1.3542 | 0.81272 | 0.35968 | 0.95352 | 0.87023 | 0.49709 | 0.87267 | 0.74493 | 1.3057 | 0.69507
regular
scale-free
>1100 Idle Cores
>2200 Idle Cores
Improve Data Transfer Costs:
Provide hardware support to effectively overlap computation with data transfers in the PIM system.
Integrate PIM-enabled memory as the main memory of the system.
Design high-speed communication channels and optimized libraries in data transfers to/from PIM-enabled memory.
Recommendation

## Slide 69
SpMV Execution on a PIM System
ColorTM
SmartPQ
SynCron
SparseP
Future Work
bus
bus
PIM-Enabled Memory
DRAM Bank
Multithreaded
PIM Core
DRAM Bank
Multithreaded
PIM Core
DRAM Bank
Multithreaded PIM Core
Host CPU
+
Load the
input vector
Execute the kernel
Retrieve the
partial results
Merge the
partial results
1
2
3
4
Main Memory
DRAM Bank
DRAM Bank

## Slide 70
Synchronization Approaches
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Multithreaded PIM Core:
Coarse-Grained (lb-cg)
Thread 1
Thread 2
Thread 3
=
output vector
Fine-Grained (lb-fg)
Thread 1
Thread 2
Thread 3
=
output vector
Lock-Free (lf)
Thread 1
Thread 2
Thread 3
=
output vector
+
=
+
Thread 1
partial results

## Slide 71
Performance of Synchronization Schemes
ColorTM
SmartPQ
SynCron
SparseP
Future Work
16 threads, 32-bit integer
Chart: Speedup
| delaunay_n13 | wing_nodal | raefsky4 | pkustk08
lb-cg | 1 | 1 | 1 | 1
lb-fg | 0.99601 | 0.99967 | 1 | 0.99978
lf | 1.2622 | 1.0821 | 1.0015 | 1.0002
Multithreaded PIM Core
24 KB
Instr. Mem.
64 KB
Data Mem.
DMA Engine
64 MB
DRAM
Bank
Fine-grained locking (lb-fg)
does not improve performance over coarse-grained locking (lb-cg)

## Slide 72
Performance of Synchronization Schemes
ColorTM
SmartPQ
SynCron
SparseP
Future Work
16 threads, 32-bit integer
Chart: Speedup
| delaunay_n13 | wing_nodal | raefsky4 | pkustk08
lb-cg | 1 | 1 | 1 | 1
lb-fg | 0.99601 | 0.99967 | 1 | 0.99978
lf | 1.2622 | 1.0821 | 1.0015 | 1.0002
Multithreaded PIM Core
24 KB
Instr. Mem.
64 KB
Data Mem.
DMA Engine
64 MB
DRAM
Bank
Fine-Grained Locking: memory accesses to the local DRAM bank are serialized in the DMA engine of the UPMEM PIM hardware.

## Slide 73
Performance of Synchronization Schemes
ColorTM
SmartPQ
SynCron
SparseP
Future Work
16 threads, 32-bit integer
Chart: Speedup
| delaunay_n13 | wing_nodal | raefsky4 | pkustk08
lb-cg | 1 | 1 | 1 | 1
lb-fg | 0.99601 | 0.99967 | 1 | 0.99978
lf | 1.2622 | 1.0821 | 1.0015 | 1.0002
Multithreaded PIM Core
24 KB
Instr. Mem.
64 KB
Data Mem.
DMA Engine
64 MB
DRAM
Bank
Improve Synchronization:
Provide low-cost synchronization mechanisms for a multithreaded PIM core.
Design hardware support to enable concurrent memory accesses to the local DRAM bank.
Integrate multiple DRAM banks per PIM core to increase execution parallelism.
Recommendation
Multithreaded PIM Core
DMA Engine
32 MB
DRAM
Bank
DMA Engine
32 MB
DRAM
Bank

## Slide 74
SpMV Execution on Various Systems
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Real PIM
System
bus
bus
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host CPU
+
Load the
input vector
Execute
the kernel
Retrieve the
partial results
Merge the
partial results
1
2
3
4
Main Memory
DRAM Bank
DRAM Bank
bus
Main Memory
DRAM Bank
DRAM Bank
Host CPU
Execute the kernel
1
CPU System
GPU System
SMX2
SMX2
Load the
input vector
Execute the kernel
Retrieve
the final vector
1
2
3
GPU Global Memory
DRAM Bank
DRAM Bank
Host CPU
GPU Cores
bus
Main Memory
DRAM Bank
DRAM Bank

## Slide 75
CPU/GPU Comparisons
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Kernel-Only (32-bit float):
  CPU = 0.51% of Peak Perf.
  GPU = 0.21% of Peak Perf.
  PIM (1D) = 50.7% of Peak Perf.
End-to-End (32-bit float):
  CPU = 4.08 GFlop/s
  GPU = 1.92 GFlop/s
  PIM (1D) = 0.11 GFlop/s
System | Cores | Peak Performance | Bandwidth | TDP
CPU | Intel Xeon Silver 4110 | 660 GFlops | 23.1 GB/s | 2x85 W
GPU | NVIDIA Tesla V100 | 14.13 TFlops | 897 GB/s | 300 W
PIM | UPMEM 1st Gen. | 4.66 GFlops | 1.77 TB/s | 379 W
Processor-
Centric
Memory-Centric
Kernel-Energy (32-bit float):
  CPU = 0.247 J
  GPU = 0.051 J
  PIM (1D) = 0.179 J

## Slide 76
CPU/GPU Comparisons
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Kernel-Only (32-bit float):
  CPU = 0.51% of Peak Perf.
  GPU = 0.21% of Peak Perf.
  PIM (1D) = 50.7% of Peak Perf.
End-to-End (32-bit float):
  CPU = 4.08 GFlop/s
  GPU = 1.92 GFlop/s
  PIM (1D) = 0.11 GFlop/s
System | Cores | Peak Performance | Bandwidth | TDP
CPU | Intel Xeon Silver 4110 | 660 GFlops | 23.1 GB/s | 2x85 W
GPU | NVIDIA Tesla V100 | 14.13 TFlops | 897 GB/s | 300 W
PIM | UPMEM 1st Gen. | 4.66 GFlops | 1.77 TB/s | 379 W
Processor-
Centric
Memory-Centric
Kernel-Energy (32-bit float):
  CPU = 0.247 J
  GPU = 0.051 J
  PIM (1D) = 0.179 J
PIM: 1.38x higher energy efficiency over CPU

## Slide 77
Core Contributions
ColorTM (ISC’18, SRC PACT’18) High-Performance Graph Coloring for CPU Systems
Graph Processing
1
SynCron (HPCA’21) A Lightweight Synchronization Mechanism for PIM Systems
Irregular
Workloads
3
SmartPQ (CF’19) An Adaptive Priority Queue for NUMA CPU Systems
Pointer-Chasing
2
SparseP (Sigmetrics’22) A Library of Efficient Sparse Matrix Vector Multiplication Kernels for Real PIM Systems
Sparse Linear Algebra
4
Thesis Statement:
Low-overhead synchronization approaches
in cooperation with well-crafted data access techniques can significantly improve performance and energy efficiency of emerging irregular applications.

## Slide 78
Thesis Summary
Processors
Cache
Main Memory
Processors
Cache
Main Memory
Irregular applications exhibit:
Inherent imbalance, random accesses, low operational intensity
Key optimization opportunities:
Lightweight synchronization + well-crafted data access policies
Time
CPUs
NUMA
CPUs
PIMs
Near-Bank
PIMs
PIM-Enabled Memory
Main Memory
Processor
Processor
Processor
PIM-Enabled Memory
Memory
Bank
Processor
Processor
Processor
Memory
Bank
Memory
Bank
ColorTM’18
1
SmartPQ’19
2
SynCron’21
3
SparseP’22
4

## Slide 79
Future Research Directions
ColorTM
SmartPQ
SynCron
SparseP
Future Work
Designing new adaptive approaches for irregular applications to capture dynamic workload demands and contention:
  Adaptive algorithmic designs
  Adaptive runtime systems
  Adaptive hardware mechanisms
Extending the techniques that we propose to accelerate irregular applications in new/unconventional systems:
  Hybrid/heterogeneous memory systems
  Disaggregated memory systems
Leveraging the key insights and recommendations that we provide to improve multiple aspects of CPU and PIM hardware and software

## Slide 80
Thesis Publications
“Combining HTM with RCU to Speed up Graph Coloring on Multicore Platforms” Christina Giannoula, Georgios Goumas, Nectarios Koziris [ISC 2018]
“An Adaptive Priority Queue for NUMA Architectures” Foteini Strati*, Christina Giannoula*, Dimitrios Siakavaras, Georgios Goumas, Nectarios Koziris [CF 2019] (* joint first authors)
“SynCron: Efficient Synchronization Support for Near-Data-Processing Architectures” Christina Giannoula, Nandita Vijaykumar, Nikela Papadopoulou, Vasileios Karakostas, Ivan Fernandez, Juan Gómez-Luna, Lois Orosa, Nectarios Koziris, Georgios Goumas, Onur Mutlu [HPCA 2021]
“SparseP: Towards Efficient Sparse Matrix Vector Multiplication on Real Processing-In-Memory Architectures” Christina Giannoula, Ivan Fernandez, Juan Gómez-Luna, Nectarios Koziris, Georgios Goumas, Onur Mutlu [ISC 2018]
“High-Performance and Balanced Parallel Graph Coloring on Multicore Platforms” Christina Giannoula, Athanasios Peppas, Georgios Goumas, Nectarios Koziris [Journal of Supercomputing 2022]

## Slide 81
Other Publications
“SMASH: Co-designing Software Compression and Hardware-Accelerated Indexing for Efficient Sparse Matrix Operations” [Kanellopoulos+, MICRO 2019]
“NATSA: A Near-Data Processing Accelerator for Time Series Analysis” [Fernandez+, ICCD 2020]
“Benchmarking Memory-Centric Computing Systems: Analysis of Real Processing-in-Memory Hardware” [Gómez-Luna+, CUT 2021]
“Benchmarking a New Paradigm: Experimental Analysis and Characterization of a Real Processing-in-Memory System” [Gómez-Luna+, IEEE ACCESS 2022]
“An MRAM-based Accelerator for Time Series Analysis” [Fernandez+, Under Submission 2022]
“Architectural Support for Efficient Data Movement in Disaggregated Systems” [Giannoula+, Under Submission 2022]
“Architecting the Processor Core and Cache Hierarchy for Systems with Monolithically-Integrated Logic and Memory” [Mansouri Ghiasi+, Under Submission 2022]

## Slide 82
PhD Scholarships & Awards
Foundation for Education and European Culture:
  September 2021 – October 2022
Hellenic Foundation for Research and Innovation +
General Secretariat for Research and Technology:
  October 2017 – March 2020
NTUA Thomaidion Awards:
  SynCron – HPCA 2021
  NATSA - ICCD 2020
  ColorTM - ISC 2018
HiPEAC Research Award:
  SynCron – HPCA 2021
2nd Place Winner at SRC Competition:
  Balanced ColorTM – SRC PACT 2018

## Slide 83
Acknowledgments
Advisors:
  Georgios Goumas, Nectarios Koziris, Onur Mutlu
Committee Members:
  Dionisios Pnevmatikatos, Stefanos Kaxiras, Dimitris Gizopoulos, Vasileios Papaefstathiou
Co-Authors and Close Collaborators
CSLab Group Members
SAFARI Group Members
Friends
Family

## Slide 84: Accelerating Irregular Applications via Efficient Synchronization and Data Access Techniques
Christina Giannoula PhD Thesis Oral
Thank you!